## Slide 1: M/M/1 queue
λn = λ, (n >=0); μn = μ (n>=1)
λ: arrival rate
μ: service rate
λ
μ

## Slide 2: Traffic intensity
rho = λ/μ
  It is a measure of the total arrival traffic to the system
    Also known as offered load
    Example: λ = 3/hour; 1/μ=15 min = 0.25 h
  Represents the fraction of time a server is busy
    In which case it is called the utilization factor
    Example: rho = 0.75 = % busy
Notes: To understand better the physical meaning of this unit, take a look at the traffic presented to a single resource. One Erlang is equivalent to a single user who uses that resources 100% of the time, or alternatively, 10 users who each occupy the resource 10% of the time. A traffic intensity greater than one indicates that customers arrive faster than they are served and is a good indication of the minimum number of servers required to achieve a stable system. For an example, a traffic intensity of 2.5 Erlangs indicates that at least three servers are required.

## Slide 3: Queuing systems: stability
λ<μ
  => stable system
λ>μ
  Steady build up of customers => unstable
Time
1 2 3 4 5 6 7 8 9 10 11
1
2
3
busy
idle
N(t)
Time
1 2 3 4 5 6 7 8 9 10 11
1
2
3
N(t)

## Slide 4: Example#1
A communication channel operating at 9600 bps
  Receives two type of packet streams from a gateway
    Type A packets have a fixed length format of 48 bits
    Type B packets have an exponentially distribution length
      With a mean of 480 bits
  If on the average there are
    20% type A packets and 80% type B packets
Calculate the utilization of this channel
  Assuming the combined arrival rate is 15 packets/s

## Slide 5: Performance measures
L
  Mean # customers in the whole system
Lq
  Mean queue length in the queue space
W
  Mean waiting time in the system
Wq
  Mean waiting time in the queue

## Slide 6: Mean queue length (M/M/1)

## Slide 7: Mean queue length (M/M/1) (cont’d)

## Slide 8: Little’s theorem
This result
  Existed as an empirical rule for many years
    And was first proved in a formal way by Little in 1961
The theorem
  Relates the average number of customers L
    In a steady state queuing system
  To the product of the average arrival rate (λ)
    And average waiting time (W) a customer spend in a system
Notes: The beauty of it lies in the fact that it does not assume any specific distribution for the arrival as well as the service process, nor does it assume any queuing discipline or depend upon the number of parallel servers in the system.

## Slide 9: LITTLE’s Formula
  : average number of messages in system
  : average delay
  λ: arrival rate
Little’s relation holds for any
  Service discipline
  Arrival process
  Holding area

## Slide 10: Graphical Proof
A(t)
  Cumulative arrival process
L(t)
  Nb. of customers that left system up to t
=> N(t) = A(t) – L(t)
  Nb. of customers in system at time t
di : interval between ith arrival and its departure

## Slide 11: Graphical Proof (continued)

## Slide 12: Graphical Proof (continued)
Now, let

## Slide 13: Mean waiting time (M/M/1)
Applying Little’s theorem

## Slide 14: Z-transform: application in queuing systems
X is a discrete r.v.
  P(X=i) = Pi, i=0, 1, …
    P0 , P1 , P2 ,…
  Properties of the z-transform
    g(1) = 1, P0 = g(0); P1 = g’(0); P2 = ½ . g’’(0)
    , +

## Slide 15: M/M/1 Queue – Infinite Waiting Room
Probability generating function
Mean
Variance

## Slide 16: M/M/S

## Slide 17: M/M/S (cont’d)

## Slide 18: M/M/S
λ
μ
S servers

## Slide 19: M/M/S: normalizing equations

## Slide 20: M/M/S: stable queue
is λ/Sμ < 1 ?
  Otherwise you will not get a stable queue, as such

## Slide 21: M/M/S: performance measures
Mean queue length
Mean waiting time in the queue (Little’s theorem)
Mean waiting time in the system
Mean # of customers in the whole system

## Slide 22: Erlang C formula
A quantity of interest
  Probability to find all s servers busy
  Ratio between Lq and Pc

## Slide 23: M/M/S: stability revisited
Stable
  If λ/Sμ < 1
Arrival rate to an individual server
Utilization of a server
Utilization of all servers

## Slide 24: M/M/1/N
Birth and death equations
λ
μ
% loss
N

## Slide 25: M/M/1/N: normalizing constant
Let ρ=λ/μ
As such
Probability of arriving
to a full waiting room

## Slide 26: M/M/1/N: what percent of λ gets into the queue?
Percentage of time the queue is full
  is equal to PN
Rate of lost customers = λ.PN
Rate of customers getting in : λ.(1-PN)
  Often referred to as effective customer arrival rate
Utilization of server
.75
.25
full
Not full

## Slide 27: M/M/1/N: performance measures
Mean # of customers in the system
Mean queue length
Waiting time in system: W = L/λ
Waiting time in queue: Wq = Lq/λ
LM/M./1

## Slide 28: M/M/1/N: equivalent systems
When an M/M/1/N queue is full
  Continuous arrival
    A system with loss
  is equivalent to shutting up the service
    For the duration during which the queue is full
    And starting it up again when system no longer ful
    This system is called a shut down system
This equivalence holds only when
  the inter-arrival is exponential

## Slide 29: Proof: rate diagrams
M/M/1/N system with loss
  Consider the special case where N = 5
0
1
2
3
4
5
λ
λ
λ
λ
λ
μ
μ
μ
μ
μ
λ

## Slide 30: Proof: rate diagrams (cont’d)
M/M/1/N shut down system
  Consider the special case where N = 5
0
1
2
3
4
5
λ
λ
λ
λ
λ
μ
μ
μ
μ
μ

## Slide 31: M/M/infinity: birth and death equations
.
.
λ
μ
Infinite number of
servers

## Slide 32: M/M/infinity: normalizing constant

## Slide 33: Erlang system: M/M/S/S
.
.
λ
μ
Finite number of
Servers = S

## Slide 34: Erlang loss formula
What percent gets in and
  What percent gets lost
PS = prob S customers in system
Effective arrival rate
Rate of lost customers = λ.PS
Erlang loss formula

## Slide 35: Erlang B formula
Probability of finding all s servers busy
In an iterative form: