## Slide 1: Machine interference problem: introduction
N machines
  Each may break down and join the repair’s man queue
    Operation time
      Exponentially distributed with rate λ
    Repair time
      Exponentially distributed with rate μ
N
machines
Repair’s man queue
1/μ
1/λ

## Slide 2: Machine interference problem: Introduction (cont’d)
Each of the N machines can be thought of
  As being a server
You get a 2 node closed queuing network
  As long as the machine holds a client called token
    The machine is operational
  # tokens = # machines
4 customers (tokens)
1/λ
1/μ

## Slide 3: Machine interference problem: history
Early computer systems
  Multiple terminals sharing a computer (CPU)
    Jobs are shifted to the computer
    Jobs run according to a Time Sharing idea
  Main performance issue
    How many terminals can I support so that
      Response time is in the order of ms
  => machine interference problem
    Operational => either thinking or typing
    Hitting the return key => machine breaks down

## Slide 4: Machine interference problem: assumptions
Problem (assumptions)
  Operative
    Mean = 1/λ
  Repair time
    Mean = 1/μ
  Repair queue
    FIFO
  Finite population of customers

## Slide 5: Machine interference problem: solution
Birth and death equations
What about P0?

## Slide 6: Normalizing constant
Rate diagram#1
  State: # of broken down machines
Rate diagram#2 (including more redundancy)
  State: # of both active and broken down machines
0
1
μ
Nλ
(N-1)λ
….
N,0
N-1,1
μ
Nλ
(N-1)λ
….

## Slide 7: Machine interference problem: performance measures
Mean repair’s man queue length
Mean # customers in the entire system
Mean waiting time (Little’s theorem)
  What is the arrival rate to the repair’s man queue?
W

## Slide 8: Arrival rate to repair’s man queue and waiting time
Arrival rate to repair’s man queue
Mean waiting time in repair’s man queue
Mean waiting in the entire repair’s man system

## Slide 9: Single machine: analysis
Cycle thru which goes a machine
Mean cycle time
Rate at which a machine completes a cycle
Rate at which all machines complete their cycle
Operational
Wait
Repair

## Slide 10: Production rate
# of repairs per unit time
  Production rate
  = rate at which you see machines
    Going in front of you

## Slide 11: Mean repair’s man queue length Lq

## Slide 12: Normalized mean waiting time
W (mean waiting time) is given by
r = average operation time/average repair time
Normalized mean waiting time
  W = 30 min, 1/μ=10 min =>
    normalized WT = 3 repair times

## Slide 13: Normalized mean waiting time: analysis
Plot the normalized waiting time
  As a function of N (# machines)
    N=1 => W=1/μ => P0 = r/(1+r)
    N is very large =>
Normalized mean waiting time
  Rises almost linearly with the # of machines
μW
N
1
N-r
1+r

## Slide 14: Mean number of machines in the system L
Plot L as a function of N
N=1 => P0 = r/(1+r)
  => L = 1/(1+r)
N is very large
  L = N - r
L
N
1/(1+r)
N-r

## Slide 15: Examples
Find the z-transform for
  Binomial, Geometric, and Poisson distributions
And then calculate
  The expected values, second moments, and variances
  For these distributions

## Slide 16: Z-transform: application in queuing systems
X is a discrete r.v.
  P(X=i) = Pi, i=0, 1, …
    P0 , P1 , P2 ,…
  Properties of the z-transform
    g(1) = 1, P0 = g(0); P1 = g’(0); P2 = ½ . g’’(0)
    , +

## Slide 17: Binomial distribution

## Slide 18: Geometric distribution

## Slide 19: Poisson distribution

## Slide 20: Problem I
Consider a birth and death system, where:
Find Pn

## Slide 21: Problem I (cont’d)
Find the average number of customers in system

## Slide 22: Problem II
In a networking conference
  Each speaker has 15 min to give his talk
    Otherwise, he is rudely removed from podium
  Given that time to give a presentation is exponential
    With mean 10 min
  What is the probability a speaker will not finish his talk?
    E[X] = 1/λ = 10 minutes => λ = 1/10
    Let T be the time required to give a presentation: a speaker will not manage
      to finish his presentation if T exceeds 15 minutes.
    P(T>15) = e-1.5

## Slide 23: Problem III
Jobs arriving to a computer
  require a CPU time
    exponentially distributed with mean 140 msec.
  The CPU scheduling algorithm is quantum-oriented
    job not completing within 100 msec will go to back of queue
  What is the probability that an arriving job will be forced to wait for a second quantum?
  Of the 800 jobs coming per day, how many
    Finish within the first quantum>

## Slide 24: Problem IV
A taxi driver provides service in two zones of a city.
  Customers picked up in zone A will have destinations
    in zone A with probability 0.6 or in zone B with probability 0.4.
  Customers picked up in zone B will have destinations in
    zone A with probability 0.3 or in zone B with probability 0.7.
  The driver’s expected profit
    for a trip entirely in zone A is 6$;
    for a trip in zone B is 8$; and
    for a trip involving both zones is 12$.
  Find the taxi driver’s average profit per trip.
    Hint: condition on whether the trip is entirely in zone A, zone B, or in both zones.

## Slide 25: Problem V
Suppose a repairman has been assigned
  The responsibility of maintaining 3 machines.
For each machine
  The probability distribution of running time
    Is exponential with a mean of 9 hours
  The repair time is also exponential
    With a mean of 12 hrs
Calculate the pdf and expected # of machines not running

## Slide 26: Problem V (continued)
As a crude approximation
  It could be assumed that the calling population is infinite
    => input process is Poisson with mean arrival rate of 3 / 9 hrs
Compare the results of part 1 to those obtained from
  M/M/1 model and an M/M/1/3 model
  Which one is a better approximation?