H.U. Fall 2009								Name: ---------------------------

PHY 218

Quiz II

1.	Take VCC  = 12v, VBE = 0.6v, and RC = 3 K

- Estimate  using the I-V curve			(  4  pts.)

- Draw the Load Line (on this sheet)		( 5 pts.)

- What is the value of IB for the VC = ½ VCC? 	( 4  pts.)

- Calculate the value of RB such that VC = ½ VCC   ( 4  pts.)

Bonus: What is the value of the nearest commercial resistor?

---------------------------------------------------------------------------------------

2.     Take Vzo = 6v, R = 200, and  r = 25.

a.	Show by direct substitution that  V = 6.8v when Vi = 20v	    	( 8  pts.)

b.	Show that for part a above     	 	Pz =  0.22 w		( 5 pts.)

c. 	Argue that for Vi = 10v , we will have 	V =  ½Vi  = 5v		( 4 pts.)

Note that “argue” means that very little calculation is necessary

--------------------------------------------------------------------------------------

- The figure shows a circuit and the I-V characteristic of the photocell.

a.  	Draw the load line and calculate the value of the current I	( 7 pts.)

b.	Why isn’t this diode operating in its linear mode?		( 5 pts.)

--------------------------------------------------------------------------------------

- Answer 8 of the following 11 questions briefly. Include a diagram wherever appropriate .   	( 8x7 = 56 pts.)

Note: The 9th answer will be ignored.

- Why does a p-n  junction have capacitance?

- Why does the Ripple Factor ( ~ 1/fCRL) decrease for large load resistance (RL) ?

Note that the formula is already given. No points for saying inversely proportional

- Why will there be no current unless photons reach the depletion zone of a photodiode?

- When will the gain of an amplifier be given by the expression  G = A/(1 + bA) ?

- Why is the reverse current in a diode independent of voltage?(see figure)

- Which factor determines the maximum current ( Izmax  )  of a Zener Diode?

- How does a Varactor diode function? Mention an application.

- Identify the circuit shown and mention a use.

- Why does CE increase the gain of an amplifier?

- Give the physical reason why IB is a small percentage of IC  (IB/IC = 1/ ~ 1/100)

- Identify the circuit shown and mention a use.

--------------------------------------------------------------------------------------------------------------------------------------------

Good Luck!								2x17 + 12 + 56 = 102