Problem I:  IP subnetting (10 minutes)

- If a host on a network has the address 172.16.45.14/30, what is the address of the subnetwork to which the host belongs?

  - 172.16.45.0

  - 172.16.45.4

  - 172.16.45.8

  - 172.16.45.12

  - 172.16.45.18

- You have a class C network, and you need ten subnets. You wish to have as many addresses available for hosts as possible. Which one of the following subnet masks should you use?

  - 255.255.255.192

  - 255.255.255.224

  - 255.255.255.240

  - 255.255.255.248

  - None of the above

- Which two of the addresses below are available for host addresses on the subnet 192.168.15.19/28 (actually, this is the IP address of a host that belongs to this subnet)? (select two answer choices)

  - 192.168.15.17

  - 192.168.15.14

  - 192.168.15.29

  - 192.168.15.31

  - None of the above

- The IP network 210.106.14.0 is subnetted using a /24 mask. How many usable networks and host addresses can be obtained from this?

- 1 network with 254 hosts

- 4 networks with 128 hosts

- 2 networks with 24 hosts

- 6 networks with 64 hosts

- None of the above

- Given that you have a class B IP address network range, which of the subnet masks below will allow for 100 subnets and 500 usable host addresses per subnet?

- 255.255.0.0

- 255.255.224.0

- 255.255.254.0

- 255.255.255.0

- None of the above

Problem II: Routing (10 minutes)

- An IP router (which does longest prefix match to route packets) has the following forwarding table mapping prefixes to outgoing interfaces:

128.2.0.0/24  (  interface 1

128.2.1.0/24  (  interface 2

128.2.2.0/24  (  interface 2

128.2.3.0/24  (  interface 3

But space in the forwarding table might be scarce. Suppose, for example, my router only has space for 3 prefixes in its forwarding table. Produce a forwarding table with only 3 entries which is equivalent to the one above – that is, each IP address will still be mapped to same outgoing interface as in the above 4-entry table. Assume the router uses the longest prefix matching to match incoming packets to interfaces.

128.2.0.0/24  (  interface 1

128.2.0.0/22  (  interface 2

128.2.3.0/24  (  interface 3

- You are given the following network prefixes:

171.64.121.0/24	171.64.180.0/24

171.64.18.0/24	171.64.181.0/24

171.64.19.0/24	171.64.187.0/24

You are to aggregate the prefixes together into the smallest possible number of shorter prefixes. What is the smallest number of prefixes and what are they?

    - 1 prefix: 171.64.179.0/21

    - 2 prefixes: 171.64.180.0/20, 171.64.18.0/21

    - 4 prefixes: 171.64.180.0/23, 171.64.187.0/24, 171.64.121.0/24, 171.64.18.0/23

    - 3 prefixes: 171.64.180.0/20, 171.64.187.0/24, 171.64.18.0/23

Problem III: Routing protocols (10 minutes)

- Consider the following network topology that we denote by G.

  - Find the shortest path from node A to each other node in G.

  - Populate the table given below with the entries found in A’s routing table? More specifically, for each destination give the neighbor to be used by A to get to that destination.

| Destination | Next hop |
| --- | --- |
| B | B |
| C | D |
| D | D |
| E | D |
| F | D |

Problem IV: TCP’s congestion window (15 minutes)

Assume a host running TCP Reno (which came after TCP Tahoe) is connected to a link with maximum segment size (MSS) of 2.5 Kbytes. The host initializes CongWin to 1 segment and Threshold to 16 segments. The round trip time RTT on this link is 50 ms.

- What is the value of CongWin after 300 msec?

  - 16 MSS

  - 15 MSS

  - 17 MSS

  - Other (give your answer): 18 MSS

- Assume a packet is sent at time = 300 msec. This packet is lost and the loss event is detected via receipt of triple duplicate ACKs.  What is the new value of CongWin?

  - 1 MSS

  - 8 MSS

  - 4 MSS

  - Other (give your answer): 9 MSS

- Assume a packet is sent at time=300 msec, is lost and a timeout occurs. What is the new value of Threshold?

  - 9 MSS

  - 8 MSS

  - 1 MSS

  - Other (provide your answer):

- Assuming a first packet loss is detected after the 9th transmission round via a timeout event, what will be the values of:

The congestion window:

  - 1 MSS

  - 8 MSS

  - 11 MSS

  - Other (put your answer):

The threshold:

- 8 MSS

- 9 MSS

- 11 MSS

- Other (put your answer): 10 MSS