## Slide 1
Chapter 7
Transformations of
Stress and Strain

## Slide 2: Introduction
Previously we were calculating stresses about specified areas that pass through a point. Here, we will consider the most general state of stress at a given point.
This part is concerned with how the components of stress are transformed under a rotation of the coordinate axes
The linear strain in the top surface of the bar is being measured by a strain gage.

## Slide 3: Introduction
The most general state of stress at a point may be represented by 6 components,
Same state of stress is represented by a different set of components if axes are rotated.
Normal
Shear
Normal
Shear

## Slide 4: Plane Stress
The free surface (not subjected to an external force) of a structural element or machine component.
Plane Stress - state of stress in which two faces of the cubic element are free of stress. For the illustrated example, the state of stress is defined by
Examples:
A thin plate subjected to forces acting in the midplane of the plate.

## Slide 5: Transformation of Plane Stress
Assume that a state of stress exists at point Q (with σz=τyz=τzx=0) defined by the stress components
Determine the stress state associated with the same element after it has been rotated through an angle about the z axis (hence σz’=τy’z’=τz’x’=0)

## Slide 6: Transformation of Plane Stress
To determine the normal stress σx’ and the shearing stress τx’y’, we consider the equilibrium conditions of a prismatic element with faces perpendicular to the x, y, and x’ axes.

## Slide 7: Transformation of Plane Stress
Solving the equations yields
Using
The expression for the normal stress σy’ is obtained by replacing θ by θ+90o

## Slide 8: Principal Stresses
The previous equations are combined to yield parametric equations for a circle,
Circle of center (σave,0) and radius R

## Slide 9: Principal Stresses
Point A: corresponds to the maximum value of σx’ and zero τx’y’
Point B: corresponds to the minimum value of σx’ and zero τx’y’
Principal stresses occur on the principal planes of stress with zero shearing stresses.

## Slide 10: Shearing Stress
Maximum shearing stress occurs for
Maximum shearing stress
θp and θs are 45o apart

## Slide 11: Example 1
7-2: For the given state of stress, determine the normal and shearing stresses exerted on the oblique face of the shaded triangular element shown. Use a method of analysis based on the equilibrium of that element, as was done in the derivations of Sec. 7.2.

## Slide 12: Example 1

## Slide 13: Example 2
7-6: For the given state of stress, determine (a) the principal planes, (b) the principal stresses

## Slide 14: Example 3
7-12: For the given state of stress, determine (a) the orientation of the planes of maximum in-plane shearing stress, (b) the maximum in-plane shearing stress, (c) the corresponding normal stress

## Slide 15: Example 4
7-22: Two members of uniform cross section 50 × 80 mm are glued together along plane a-a, that forms an angle of 25o with the horizontal. Knowing that the allowable stresses for the glued joint are σ = 800 kPa and τ = 600 kPa, determine the largest centric load P that can be applied

## Slide 16: Example 4

## Slide 17: Example 5
7-25: A mechanic uses a crowfoot wrench to loosen a bolt at E. Knowing that the mechanic applies a vertical 100 N force at A, determine the principal stresses and the maximum shearing stress at point H located as shown on top of the 18 mm diameter shaft.

## Slide 18: Example 5

## Slide 19: Example 5

## Slide 20: Example 6
7-26: The steel pipe AB has a 102 mm outer diameter and a 6 mm wall thickness. Knowing that the arm CD is rigidly attached to the pipe, determine the principal stresses and the maximum shearing stress at point K.

## Slide 21: Example 6

## Slide 22: Example 6

## Slide 23: Mohr’s Circle for Plane Stress
For a known state of plane stress σx, σy and τxy, plot the points X and Y and construct the circle centered at C.
The circle can be used to calculate the stress state of an element at any orientation.
The principal stresses are obtained at A and B.
The direction of rotation of Ox to Oa is the same as CX to CA.

## Slide 24: Mohr’s Circle for Plane Stress
With Mohr’s circle uniquely defined, the state of stress at other axes orientations may be depicted.
Normal and shear stresses are obtained from the coordinates X’Y’.
For the state of stress at an angle θ (cw) with respect to the xy axes, construct a new diameter X’Y’ at an angle 2θ (cw) with respect to XY.

## Slide 25: Mohr’s Circle for Plane Stress
Mohr’s circle: Centric axial loading
Points D and E yield the orientation of the planes of maximum shearing stress

## Slide 26: Mohr’s Circle for Plane Stress
Mohr’s circle: Torsional loading
Points A and B define the principle planes and yield the principle stresses

## Slide 27: Example 7
7-36: For the given state of stress, determine using Mohr’s circle the normal and shearing stresses after the element shown has been rotated through (a) 25o clockwise, (b) 10o counterclockwise.

## Slide 28: Example 7

## Slide 29: Example 8
7-44: Two members of uniform cross section 50 × 80 mm are glued together along plane a-a, that forms an angle of 25o with the horizontal. Knowing that the allowable stresses for the glued joint are σ = 800 kPa and τ = 600 kPa, determine the largest centric load P that can be applied using Mohr’s circle.

## Slide 30: Example 8

## Slide 31: Example 9
7-55: Determine the principal planes and the principal stresses for the state of plane stress resulting from the superposition of the two states of stress shown.

## Slide 32: Example 9

## Slide 33: General State of Stress
State of stress at Q defined by:
Consider the general 3D state of stress at a point and the transformation of stress associated with element rotation. Our analysis will be limited to the determination of σn on a plane of arbitrary orientation.

## Slide 34: General State of Stress
Consider the tetrahedron with a face perpendicular to the line QN with direction cosines
The forces exerted on ABC consist of a normal force σn ΔA directed along QN and of a shearing force of magnitude τ ΔA perpendicular to QN

## Slide 35: General State of Stress
The statics requirements lead to
Dividing by ΔA
and
solving for σn

## Slide 36: General State of Stress
Now select the axes in such a way that the right-hand member reduces to the three terms containing the squares of the direction cosines
The coordinate axes a, b, c are referred to as the principal axes of stress. The corresponding coordinate planes are known as the principal planes of stress and the corresponding normal stresses σa, σb, and σc as the principal stresses at Q.

## Slide 37: Mohr’s Circle 3D Analysis of Stress
Circle AB rotation about the principle axis Qc
Circle BC rotation about the principle axis Qa
Circle AC rotation about the principle axis Qb
The transformation about any different axis will lead to a stress state defined by a point in the shaded area.

## Slide 38: Mohr’s Circle 3D Analysis of Stress
The three circles represent the normal and shearing stresses for rotation around each principal axis.
Radius of the largest circle yields the maximum shearing stress.

## Slide 39: Mohr’s Circle 3D Analysis of Stress
Points A and B (representing the principal planes) are on opposite sides of the origin O.
  The corresponding principal stresses are the maximum and minimum normal stresses for the element
  The maximum shearing stress for the element is equal to the maximum “in-plane” shearing stress
  The planes of maximum shearing stress are at 45o to the principal planes.
Plane stress case: the z axis is a principal
Case I:

## Slide 40: Mohr’s Circle 3D
  The planes of maximum shearing stress correspond to points D and E, and are at 45o to the principal planes.
Plane stress case: the z axis is a principal

## Slide 41: Mohr’s Circle 3D Analysis of Stress
Points A and B (representing the principal planes) are on the same sides of the origin O.
  The circle defining σmax, σmin, and τmax for the element is not the circle corresponding to transformations within the plane of stress
  The maximum shearing stress for the element is equal to half of the maximum stress
  The planes of maximum shearing stress are at 45o to the plane of maximum normal stress
Plane stress case: the z axis is a principal
Case II:

## Slide 42: Mohr’s Circle 3D
  The normals Qd’ and Qe’ to the planes of maximum shearing stress are obtained by a 45o rotation about the Qb axis of the Qa or the Qc axis.
Plane stress case: the z axis is a principal

## Slide 43: Example 10
7-68: For the state of stress shown, determine the maximum shearing stress when (a) σy = 40 MPa, (b) σy = 120 MPa. (Hint consider both in-plane and out-of-plane shearing stresses.)

## Slide 44: Example 10

## Slide 45: Example 11
7-71: For the state of stress shown, determine the maximum shearing stress when (a) σz = 0 MPa, (b) σz = 60 MPa, (c) σz = -60 MPa.

## Slide 46: Example 11

## Slide 47: Example 12
7-75: For the state of stress shown, determine the value of τxy for which the maximum shearing stress is (a) 63 MPa, (b) 84 MPa.

## Slide 48: Example 12

## Slide 49: Example 13
7-79: For the state of stress shown, determine two values of σy for which the maximum shearing stress is 80 MPa.

## Slide 50: Example 13