EECE 210

Quiz 3, November 23, 2013

4% (Primal Question)

A.	Express the voltage 2cos(100t – 30() V as a phasor and show it on a phasor diagram, taking the function cos100t as the reference.

Solution: Considering the function as Vmcos(100t – (() V, V = Vm(-(( V.

Version 1: Vm = 2 V, ( = 30(

Version 2: Vm = 3 V, ( = 60(

Version 3: Vm = 4 V, ( = 90(

Version 4: Vm = 5 V, ( = 120(

Version 5: Vm = 6 V, ( = 150(.

4% (Primal Question)

B.	Determine Zeq as the sum of a resistance and a reactance, given R = 10 (.

Solution: (30||-j40) =  ; Zeq = (19.2 + R) – j14.4 (.

Version 1: R = 10 (, Zeq = (19.2 + R) – j14.4 ( = 29.2 – j14.4 (

Version 2: R = 20 (, Zeq = (19.2 + R) – j14.4 ( = 39.2 – j14.4 (

Version 3: R = 30 (, Zeq = (19.2 + R) – j14.4 ( = 49.2 – j14.4 (

Version 4: R = 40 (, Zeq = (19.2 + R) – j14.4 ( = 59.2 – j14.4 (

Version 5: R = 50 (, Zeq = (19.2 + R) – j14.4 ( = 69.2 – j14.4 (.

4% (Primal Question)

C.	Determine VO, given VSRC = 10(0( V.

Solution: VO = (VSRC/j10)(j5 = VSRC/2 V.

Version 1: VSRC = 10(0( V, VO = 5(0( V

Version 2: VSRC = 20(0( V, VO = 10(0( V

Version 3: VSRC = 30(0( V, VO = 15(0( V

Version 4: VSRC = 40(0( V, VO = 20(0( V

Version 5: VSRC = 50(0( V, VO = 25(0( V.

4% (Primal Question)

D.	Determine VO and I1, given VSRC = 1(0( V.

Solution: VO = -4VSRC, I2 = 4 VSRC/1 mA; I1 = 4I2 = 16VSRC mA.

Version 1: VSRC = 1(0( V, VO = -4(0( V, I1 = 16(0( mA

Version 2: VSRC = 2(0( V, VO = -8(0( V, I1 = 32(0( mA

Version 3: VSRC = 3(0( V, VO = -12(0( V, I1 = 48(0( mA

Version 4: VSRC = 4(0( V, VO = -16(0( V, I1 = 64(0( mA

Version 5: VSRC = 5(0( V, VO = -20(0( V, I1 = 80(0( mA.

4%

1.	Determine i as a function of time, given vSRC = 10sin(100t + 15() V.

- A

- A

- A

- A

Solution:  (L = 100(0.2 = 20 (. The circuit in the frequency domain is as shown.  =  V. It follows that  A.

Version 1: Vm = 10 V,  A

Version 2: Vm = 20 V,  A

Version 3: Vm = 30 V,  A

Version 4: Vm = 40 V,  A

Version 5: Vm = 50 V,  A.

4%

2.	Determine Zeq.

- -j2 (

- -j (

- j0.5 (

- j (

- 2 – j3 (

Solution: The bridge is balanced, so that the 10 ( resistor does not carry current, and can be replaced by an open circuit or a short circuit. If open circuited, the impedance of each of the two paralleled branches is -j2 (, which gives Zeq = -j (.

4%

3.	Given two identical coils wound on a core of high permeability, each of inductance 1 H, the coefficient of coupling being 0.5. Determine the flux linkage in one coil when this coil is open circuited and the current in the other coil is 1 A.

- 2.5 Wb-T

- 1 Wb-T

- 0.5 Wb-T

- 1.5 Wb-T

- 2 Wb-T

Solution: M =  H; ( = Mi = 0.5(1 = 0.5 Wb-T

Version 1: i = 1 A, ( = 0.5i = 0.5 Wb-T

Version 2: i = 2 A, ( = 0.5i = 1 Wb-T

Version 3: i = 3 A, ( = 0.5i = 1.5 Wb-T

Version 4: i = 4 A, ( = 0.5i = 2 Wb-T

Version 5: i = 5 A, ( = 0.5i = 2.5 Wb-T.

4%

4.	Determine Zeq, given R = 5 (.

- 5 + j5 (

- 5 – j5 (

- 0

- j10 (

- 5 (

Solution: If the linear transformer is replaced by its T-equivalent circuit, the circuit becomes as shown. The impedance of j5 ( – j5 ( is zero. This in parallel with j5 ( is zero, and in series with zero is zero. It follows that Zeq = R.

Version 1: R = 5 (, Zeq = 5 (

Version 2: R = 10 (, Zeq = 10 (

Version 3: R = 15 (, Zeq = 15 (

Version 4: R = 20 (, Zeq = 20 (

Version 5: R = 25 (, Zeq = 25 (.

4%

5.	Determine the phase angle of the phasor current I2 with respect to the phase angle of the phasor current I1.

- 0

- 90( leading

- 90( lagging

- 180( leading.

- 180( lagging

Solution: V1 and V2 are in phase and may be drawn along the real axis. , the current in the capacitor due to V2 leads V2 by 90( and is in phase with I1; I2 = -. I2 therefore lags I1 by 180(.

4%

6.	Determine IS, given VSRC = 10(0( V.

- 2(0( A

- 4(90( A

- 4(-90( A

- 2(45( A

- 2(-45( A

Solution: The induced voltages in the two windings, being equal and opposite, add to zero. It follows that IS = VSRC/5 A.

Version 1: VSRC = 10(0( V, IS = VSRC/5 A = 2(0( A

Version 2: VSRC = 15(0( V, IS = VSRC/5 A = 3(0( A

Version 3: VSRC = 20(0( V, IS = VSRC/5 A = 4(0( A

Version 4: VSRC = 25(0( V, IS = VSRC/5 A = 5(0( A

Version 5: VSRC = 30(0( V, IS = VSRC/5 A = 6(0( A.

20%

7.	Determine VO using superposition. (10 grades per component)

Solution: If the 10(-45( V source is applied alone, with the other source replaced by a short circuit, the circuit becomes as shown. The impedance seen by the source is (20||(-j20)) + (20||j20) = =  20 (. The source current is 0.5(-45( A, and VO1 = (0.5(-45()((20||j20) =   V.

If the 10(0( V source is applied alone, with the other source replaced by a short circuit, the -j20 ( impedance is paralleled with the j20 ( impedance. The parallel impedance is , and the circuit reduces to that shown. It follows from voltage division that VO2 = 5(0( V. From superposition, VO =  V.

20%

8.	Derive the mesh-current equations for the circuit shown. DO NOT SOLVE THESE EQUATIONS.

Solution: Mesh 1:

(j30 + j10)I1 – j10I2 – (j30 – j20)I3 =

20(50(

Mesh 2: -j10I1 + (50 + j10 – j30)I2

-(50 + j20)I3 = 0

Mesh 3: -(j30 – j20)I1 – (50 + j20)I2 + (50 + j30 + j20)I3 = 0

20%

9.	Determine the power dissipated in the 30 ( resistor, given vSRC = 30cos(10t + 15() V (15 grades for iO and 5 grades for power).

Solution: The circuit in the frequency domain is as shown. KVL around the mesh on the LHS gives: 15IO + V1 = 30(15(. For the load, 2V1 = 30IO, or V1 = 15IO. Substituting for V1, IO = 1(15( A. The rms value of current is 1/ A. The power dissipated in the 30 ( resistor is 30/2 = 15 W.