Physics210 revision for quiz 1

Things to memorize:

- Unit of a force: 1Kg . m / s2 = 1 N=1 Newton

- work exerted by spring (Hooke’s law)

- and

- If there is  a force of friction acting, we can extend the work-kinetic energy theorem as:

- Average power

- Instantaneous power  but

- GPE:

- Work done on the system equal to the change in the gravitational potential energy.

- Conservation of mechanical energy

- (  Changes in Mechanical Energy for Non-conservative Forces

- density:

- pressure: Fluid assumed at rest exerts a force perpendicular to a surface in contact with it  if  pressure  varies over the surface ,  if P is the same over the surface

- Pressure as a function of height (static fluid)

- pressure difference between two levels in a fluid:

- Pascal’s law: Pressure applied to an enclosed incompressible fluid is transmitted undiminished to all parts of the fluid. This is independent of the shape of the vessel

- pressure of the atmosphere as a function of the height The pressure decreases exponentially with the height

- Barometer:      in vacuum

- If p0= 1.013x105 pa   then

- Open-Tube Manometer:  (

- Archimedes Principle: If a body, completely or partially immersed in a fluid, the fluid exerts an upward buoyant force equal to the weight of the fluid displaced by the body.

- Buoyancy:

- Two cases to be considered: a. Totally submerged body

- b. Floating: In case of floating

- The buoyant force is exerted by the fluid. It is influenced by the amount of fluid displaced by the object, not by its density.

- Motion of sub immersed body in a fluid is determined by the densities of the object and fluid

- Force on dam:

- Net Work:

- Change in kinetic energy:

- Change in potential energy:

- Work-Energy Theorem:

- Bernoulli’s Equation:

- This equation indicates that:

1. The pressure of the fluid decreases as the speed of the fluid increases.

2. The pressure of the fluid decreases with increasing elevation.

Therefore you need a water pump in your apartment in a high floor

- Torricelli’s Law:

An enclosed tank containing a liquid of density has a hole at a distance y1 from its bottom. The hole is open to atmosphere (p1=p0) and A1 much smaller than A2.

Suppose the air above the liquid is p (at level 2 in the Figure). Determine the speed of the liquid through the hole when the liquid level is h above the hole.

Solution: A2 large means velocity is very small there : v2=0.

Now apply Bernoulli’s equation:  =>

- Using Bernoulli's equation:

P1 + (1/2) ( v12 = P2 + (1/2) ( v22

But                  A1 v1 = A2  v2     =>

- Definition of the surface tension:

- Given:    mass of the strider m=2x10-5 Kg,

radius of his foot assumed circular: r=1.5x10-4 m

What is then the angle (, if the strider does not sink?