Date: 11 April 2007

Physics 211L

The Construction of a Digital Multi-meter

Name:				Section number: 1

Name:             			Instructor: Ms. Sara Najm

- Resistance Box:

Draw the circuit of the Resistance box, including resistance values

B. Digital Multi-Meter

|  | Meter Reading | VR124 (measured) | Meter Reading | VR500 (measured) | Voltmeter Resolution |
| --- | --- | --- | --- | --- | --- |
| V1(B1-B2) | 12.3 (mV) | 1.230 V | 50.6 (mV) | 5.06 | 0.01 |
| V2(B1-B3) | 122.4 (mV) | 1.224 V | --------- | --------- | 0.001 |
| V3(B1-B4) | ---------- | ---------- | --------- | --------- | --------- |
| V(nominal) | -------------- | 1.24 V | -------------- | 5.00 V | -------------- |

- Voltage Measurement:

- How do the nominal voltages compare to the measured ones? Calculate the relative error between the most precise reading for VR124 and VR500 and the nominal voltage values.

B1-B2 = 10000 Ω

B2-B3= 90000 Ω

B3-B4 = 900000 Ω

- VDVM =12.3 mV

For VR124

For VR500

- VDVM  = 122.4 mV

For VR124

For VR124

The most precise value of Vx= 1.224 V

1.224-0.001=1.223

1.224+0.001=1.225

1.24 does not lie between these two values. This means that the calculated voltage is not accurate.

For VR500

The most precise value of Vx= 5.06 V

5.06-0.01=5.05

5.06+0.01=5.07

5 does not lie between these two values. This means that the calculated voltage is not accurate.

2) What is the largest voltage you can measure with your voltmeter?

Vx = max when VDVM  =max     and 	R is max between B1-B4

3) What is the resistance of your voltmeter?

- Current Measurement:

|  | Meter Reading | IR120 Measured Current | Ammeter Resolution |
| --- | --- | --- | --- |
| V1(across1Ω) | 12.4 mV | 12.4 mA | 0.1 |
| V2(across10Ω) | 117.3 mV | 11.73 mA | 0.01 |
| V3(across100Ω) | ----------- | ----------- | ----------- |
| I(nominal) | -------------- | 12.0 mA | -------------- |

|  | Meter Reading | IR088 Measured Current | Ammeter Resolution |
| --- | --- | --- | --- |
| V1(across1Ω) | 0.9 | 0.9 mA | 0.1 |
| V2(across10Ω) | 8.8 | 0.88 mA | 0.01 |
| V3(across100Ω) | 87.2 | 0.872 mA | 0.001 |
| I(nominal) | --------------- | 0.88 mA | ------------- |

- How do the nominal current values compare to the measured ones? Calculate the relative error between the most precise reading for IR088 and IR120 and the nominal current values.

The most precise value for IR120 is 11.73 mA.

11.73-0.01=11.72

11.73+0.01=11.74

12 does not lie between the two values. This means that the calculated voltage is not accurate.

The most precise value for IR088 is 0.872 mA.

0.872-0.001=0.871

0.872+0.001=0.873

0.88 does not lie between these two values. This means that the calculated voltage is not accurate.

2) What is the largest current you can measure with your ammeter?

The current is maximum when R is minimum so  R = 1 Ω .

The current is maximum when V is maximum Vmax =199.9 mV

- Resistance Measurement:

For this part, the nominal values of the resistance can be read from the color-coded bands on the resistors.

|  | Meter Reading | Measured Resistance (Ω) | Ohm-meter Resolution |
| --- | --- | --- | --- |
| V1(10μA) | 183 mV | 18300 Ω | 1 |
| V2(100μA) | ---------- | ------------- | ------------ |
| R(nominal) | Rx=18000 Ω | -------------- | -------------- |

|  | Meter Reading | Measured Resistance (Ω) |
| --- | --- | --- |
| V1(10μA) | 12 mV | 1200 Ω |
| V2(100μA) | 120.3 mV | 1203 Ω |
| R(nominal) | Ry=1200 Ω | -------------------- |

Series resistors

|  | Measured Voltage | Measured Resistance (Ω) |
| --- | --- | --- |
| V1(10μA) | 195 mV | 19500 Ω |
| V2(100μA) | ---------------------- | ----------------- |
| Rx & Ry = 19200 Ω | ------------------------ | ------------------ |

Parallel resistors

|  | Measured Voltage | Measured Resistance (Ω) |
| --- | --- | --- |
| V1(10μA) | 11.3 mV | 1130 Ω |
| V2(100μA) | 112.8 mV | 1128 Ω |
| Rx // Ry = 1125 Ω | ------------------------ | ------------------ |

- How do the nominal resistance values compare to the measured ones?

Rx =18300 Ω

Rnominal = 18000 Ω

18300-1=18299

18300+1=18301

Rnominal does not lie between the two values. The calculated value is not accurate.

Ry =1200 Ω

Rnominal = 1200 Ω

1200-1=1199

1200+1=1201

Rnominal lies between the two values. Thus, thee calculated value is accurate.

Ry = 1203 Ω

Rnominal = 1200 Ω

1203-1=1202

1203+1=1204

Rnominal does not lie between the two values. The calculated value is not accurate.

- How do the values of the series and parallel combinations compare to the values calculated using the measured values of Rx and Ry?

Rx+Ry =19500 Ω

Rnominal = 19200 Ω

19500-1=19409

19500+1=19501

Rnominal does not lie between the two values. The calculated value is not accurate.

Rx // Ry = 1130 Ω

Rnominal = 1125 Ω

1130-1=1129

1130+1=1131

Rnominal does not lie between the two values. The calculated value is not accurate.

Rx // Ry = 1128 Ω

Rnominal = 1125 Ω

1128-1=1127

1128+1=1129

Rnominal does not lie between the two values. The calculated value is not accurate.

3) What is the largest resistance you can measure with your ohmmeter?

For R to be maximum, V should be maximum and I should be minimum.

.

# Text boxes

Grade: