Date:_17/05/2007_

Physics 211L

RLC circuits

Name: _	                          Section number: _1_

Partner’s Name: _ _	              Instructor: _Ms. Sara Najm_

Calculate the resonance frequency from eq(3): = 10.38 Khz.

- Determination of the resonant frequency of an RLC circuit:

i- DRB at 300	 Vin=10.0V (peak-to-peak)

Note that Vin decreases slightly around resonance. You must adjust Vin to 10.0 V at every measurement

| Frequency (Hz) | Frequency (Hz) | Vout (V) |
| --- | --- | --- |
| fres– 7.0 kHz | 3.78 | 0.46 V |
| fres– 5.0 kHz | 5.78 | 0.64 V |
| fres– 3.5 kHz | 7.28 | 1 V |
| fres– 2.5 kHz | 8.28 | 1.55 V |
| fres– 2.0 kHz | 8.78 | 1.9 V |
| fres– 1.5kHz | 9.28 | 2.3 V |
| fres– 1.2 kHz | 9.58 | 2.5 V |
| fres–0.9 kHz | 9.88 | 2.8 V |
| fres–0.6 kHz | 10.18 | 3 V |
| fres–0.4 kHz | 10.38 | 3.1 V |
| fres –0.2 kHz | 10.58 | 3.2 V |
| fres | 10.78 | 3.3 V |
| fres + 0.2 kHz | 10.98 | 3.2 V |
| fres + 0.4 kHz | 11.18 | 3.1 V |
| fres + 0.6kHz | 11.38 | 3 V |
| fres+ 0.9 kHz | 11.68 | 2.8 V |
| fres+ 1.2 kHz | 11.98 | 2.6 V |
| fres+ 1.5 kHz | 12.28 | 2.4 V |
| fres+ 2.0 kHz | 12.78 | 2 V |
| fres+ 2.5 kHz | 13.28 | 1.9 V |
| fres+ 3.5 kHz | 14.28 | 1.5 V |
| fres+ 5.0kHz | 15.78 | 1.2 V |
| fres+ 7.0 kHz | 17.78 | 0.9 V |

Plot the graph of Vout versus frequency.

Vary the frequency in order to locate the frequencies at which Vout reaches 0.707 of its resonance value. Remember that Vin must remain constant.

Measure the resistance of the inductor, RL, and calculate Q, using equation 3 in the manual.

RL = 108.68 .			L = 50mH

R= RL + 300 = 408.68 Ω

How do the calculated and measured values of Q compare?

7.89 + 0.01 = 7.9

7.89 – 0.01 = 7.88

4.364 is not between 7.9 and 7.88 which means that our measurement is not accurate.

ii- DRB at 10	 Vin=10.0V (peak-to-peak)

| Frequency (Hz) | Frequency (Hz) | Vout (V) |
| --- | --- | --- |
| fres– 7.0 kHz | 3.792 | 13.5 mV |
| fres– 5.0 kHz | 5.792 | 22.5 mV |
| fres– 3.5 kHz | 7.258 | 38 mV |
| fres– 2.5 kHz | 8.293 | 56 mV |
| fres– 2.0 kHz | 8.791 | 95 mV |
| fres– 1.5kHz | 9.291 | 87.5 mV |
| fres– 1.2 kHz | 9.593 | 102.5 mV |
| fres–0.9 kHz | 9.899 | 117.5 mV |
| fres–0.6 kHz | 10.201 | 140 mV |
| fres –0.4 kHz | 10.392 | 145 mV |
| fres - 0.2 kHz | 10.588 | 155 mV |
| fres | 10.795 | 150 mV |
| fres + 0.2 kHz | 10.991 | 157.5 mV |
| fres + 0.4 kHz | 11.195 | 150 mV |
| fres + 0.6kHz | 11.355 | 140 mV |
| fres+ 0.9 kHz | 11.695 | 125 mV |
| fres+ 1.2 kHz | 11.993 | 115 mV |
| fres+ 1.5 kHz | 12.295 | 100 mV |
| fres+ 2.0 kHz | 12.791 | 85 mV |
| fres+ 2.5 kHz | 13.292 | 75 mV |
| fres+ 3.5 kHz | 14.247 | 57.5 mV |
| fres+ 5.0kHz | 15.766 | 45 mV |
| fres+ 7.0 kHz | 17.835 | 32 mV |

Plot the graph of Vout versus frequency.

Vary the frequency in order to locate the frequencies at which Vout reaches 0.707 of its resonance value. Remember that Vin must remain constant.

Calculate Q, using equation 3 in the manual.

How do the measured and calculated values of Q compare?

RL = 108.68 .			L = 50 mH

R= RL + 10 = 118.68Ω

77.211 – 0.001 = 77.21

77.211 + 0.001 = 77.212

1.15 is not between 77.21 and 77.212 which means that our measurement is not precise.

### Questions and Analysis

Compare the two Vout versus frequency graphs and comment.

The two Vout versus frequency graphs are somehow similar. But F+ and F- greatly vary from one graph to the other. In the first graph (R = 408.68 Ω), F+= 12.32 and F- = 9.85. While in the second graph (R = 108.68 Ω), F+= 6.5 and F- = 15.87.

- Phase measurements using lissajoux figures:

DRB at 300 :

Find the phase angle between Vin and Vout by measuring A and D for the following frequencies:

| Frequency (Hz) | D | A | Φ = sin-1(D/A) | Φ (calculated from (1) |
| --- | --- | --- | --- | --- |
| fres /2 | 0.5 | 0.55 | 65.38º | 85.2º |
| f - | 1.7 | 2.25 | 49.07º | 59º |
| fres | 0.3 | 3 | 5.74º | 0º |
| f+ | 1.2 | 2.25 | 32.23º | 69.88º |
| 2fres | 0.6 | 0.65 | 67.38º | 89.99º |

How do the measured and calculated phase differences compare?

For fres /2:

85.2 + 0.1 = 85.3

85.2 – 0.1 = 85.1

65.38 is not between 85.1 and 85.3 which means that our measurement is not accurate.

For f -:

59 + 1 = 60

59 – 1 = 58

49.07 is not between 58 and 60 which means that our measurement is not accurate.

For fres:

0 + 1 = 1

0 – 1 = -1

5.74 is not between -1 and 1 which means that our measurement is not accurate.

For f+:

69.88 + 0.01 = 69.89

69.88 – 0.01 = 69.87

32.23 is not between 69.87 and 69.87 which means that our measurement is not accurate.

For 2fress:

89.99 + 0.01 = 90

89.99 – 0.01 = 89.98

67.38 is not between 89.98 and 90 which means that our measurement is not accurate.

# Text boxes

| f+ | 12.32 Khz |
| --- | --- |
| f- | 9.85 Khz |
| Qmeasured | 3.49 C |

| F+ | 6.5 Khz |
| --- | --- |
| F - | 15.87 Khz |
| Qmeasured | 7.24 |

Grade: