- Draw a FBD (8%)

- Compute Cable EC force (14%)

∑ M about B = 0,

10*sqrt(2) * T – F*20 = 0

T = 200 sqrt(2) = 282N

- Compute Reactions at E and B (magnitude and direction) (14%)

Reaction at E: Re = T = 282N          along T

Reaction at B: Optimum equation ∑ M about G = 0, still we can use:

∑ Fy = 0,

V - F + T*sqrt(2)/2 = 0

V = 200-200*2/2 = 0

- Compute spring AB force and deformation (indicate tension or compression, elongation or shortening) assuming spring stiffness K=200 N/cm (14%): Optimum equation ∑ M about H = 0, still we can use:

∑ Fx = 0,

-Ts – T * sqrt(2)/2 = 0

Ts = -200N = 200N compression

Δ = 200/200 cm = 1cm shortening

# Text boxes

F = 200N

T

Ts

45°

10

10

V

B

C

D

G

H