PHYSICS 211

Quiz II

TIME: 60 minutes

December 14, 2010

#### DO NOT OPEN THIS EXAM BEFORE YOU ARE TOLD TO BEGIN

NAME________________________________________________

ID Number ________________________

### Useful information

0=8.85x10-12 C2/N.m2.

#### Grading

| Problem 1 |  |
| --- | --- |
| Problem 2 |  |
| Problem 3 |  |
| TOTAL |  |

Problems

1.(40%)

Consider a battery with a potential difference V connected to a cylindrical conductor with length l and a cross-section A.

(a) (7%)  Determine the velocity of one electron as a function of time assuming that it makes no collisions.

- (5%) When collisions are taken into account, briefly describe the necessary modifications that are to be undertaken for the velocity and time?

- (10%) Determine the relation between the current density j and the electric field E

- (10%) Determine Ohm’s law, the relation between the current I and the potential difference V

- (6%) Comment on the relationship obtained and the proportionality constants between j and E and I and V.

- (7%) What happens if there were no collisions?

2. (20%)

(a) (10%) Demonstrate that if three resistors are connected in parallel, then the expression of the equivalent capacitor is

1/Req = 1/R1 + 1/R2 + 1/R3

(b) (10%) Demonstrate that if three resistors are connected in series, then the expression of the equivalent capacitor is

Req = R1 + R2 + R3

3. (40%) Using Kirchhoff’s rules,

(a)(20%) find the current in each resistor in the Figure above.

(b)(10%) Find the potential difference between points c and f. Which point is at the higher potential?

(c) (10%) Re-determine the currents in the circuit long after (fully charged) including a capacitor between R2 and E2

##### SCRATCH PAPER

Nothing on this page will be graded