American University of Beirut

Electrical and computer engineering department

EECE 312

Problem session 4  		3/11/2008

Chapter 10 problems 7, 21, 23,  37, 48

Solution:

first method, you can solve the problem without thevenin: write KCL: ix = ix/2 +i ==> i=ix/2, then write KVL: 5-ix*1kohm -v=0 ==>  5 - 2*i -v=0  This is the load line that you can draw on the diode charcteristic for graphical analysis.

second method: to find thevenin eq. circuit:

open the diode and find v across the o.c. (= Vth). Since in this case, you will have ix and ix/2 flowing in the same loop, then ix =0, and v = Vth=5V.

to get Rth, zero the voltage source, and apply at the place of the diode a Vtest, and call the current going out of it Itest. Rth = Vtest/Itest.

in this circuit, Vtest = -ix*1kohm,  and itest + ix = ix/2 (KCL) therefore

itest = -ix/2. replace in Vtest : Vtest = 2*itest therefore Rth = Vtest/Itest=2kohm.