PHYS 210 L

The Spectrometer

I. DIFFRACTON GRATING:

A. Incandescent lamp:

# Illuminate the slit

a) Describe the spectrum after looking at it.

We see a continuous spectrum containing the whole range of visible colors from violet to red. Colors appear in the following order as we move the telescope from the initial position: Violet, Blue, Green, Yellow, Orange and Red.

b) Angles measured in the first order:

Extreme red: 23 degrees and 30 minutes.

Extreme violet: 14 degrees and 42 minutes.

c) Wavelengths:

Using the formula d.sin( = m.( , with m=1, and d = (1/600) mm, we find the following:

 Extreme red: 664.5818 nm

Extreme violet: 422.9299 nm

B. Mercury Lamp:

a) Describe the spectrum you observe. What can you say about the mercury source?

Through the telescope, we can observe the emission spectrum of the mercury:

We find several colors distributed in a discontinuous way as strips in the following order:

Violet, indigo, bluish green, phosphoric green, orange and red.

b)

| Sharp line | I | II | III | IV | V | VI | VII |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Angle (deg) |  |  |  |  |  |  |  |
| Color | Violet | Indigo | Bluish Green | Phosphoric Green | Orange | Orange | Red |
| Wavelength (nm) | 404.614 | 446.332 | 501.639 | 557.259 | 590.938 | 596.375 | 638.701 |

II. Prism:

# Mercury spectrum

Number of orders per color: 1

The most deviated color: Violet.

Minimum Deviation:

| Color () | Violet | Indigo | Bluish Green | Phosphoric Green | Orange | Red |
| --- | --- | --- | --- | --- | --- | --- |
| Angle |  |  |  |  |  |  |
| n() | 1.543 | 1.538 | 1.532 | 1.528 | 1.526 | 1.526 |

Plot n() versus .