American University of Beirut

Department of Electrical and Computer Engineering

EECE 320 – Digital Systems Design

Assignment 1

Due 19-9-14 at 11am in class

Suggested problems: Solve the drill problems of chapter 2.

Problem 1: Complete the following table. Numbers are signed except when they are listed in the Unsigned Binary column. Use the necessary number of bits.

| Decimal | Octal | Hex. | Unsigned Binary | Signed-Magnitude representation | Signed 1’s complement representation | Signed 2’s complement representation |
| --- | --- | --- | --- | --- | --- | --- |
| +51.75 |  |  |  |  |  |  |
| -42.125 |  |  |  |  |  |  |
| +75 |  |  |  |  |  |  |
| -63 |  |  |  |  |  |  |
|  |  |  | 11100101 |  |  |  |
|  |  |  |  | 10110100 |  |  |
|  |  |  | 01011001 |  |  |  |

Problem 2: Find the 9’s complement of the decimal number 5678.

prove that 7261 – 5678 can be found as 7261 plus the 10’s complement of 5678.

Problem 3:  Assuming those are signed numbers written in 2’s complement representation compute using 2’s complement arithmetic, and using 8 bits:

- 011011 – 110110

- 10110 – 101011

Problem 4: Add the following Hexadecimal numbers:

4B5C7A5F + 2CBF678A

Problem 5: Add the following BCD numbers and verify your result by performing the corresponding decimal operation (hint: if the sum of two BCD digits is larger than 9 add 6 to this sum to get the result as a BCD digit):

1001+0101;	0110+0111;	1001+1000;	0111 1001 + 0110 0111