American University of Beirut

Department of Electrical and Computer Engineering

EECE 320 – Digital Systems Design

Dr. Lama Hamandi			Assignment 2 		due 17/10/2011

1) Prove the following identity using a truth table:

A’ + AX’Y + AXZ + AYZ = A’ + X’Y + XZ

2)  Obtain the truth table of the following function and express it in canonical sum of minterms, the ∑ notation, canonical product of maxterms, the ∏ notation.

F = A’ + AX’Y + AXZ + AYZ

3) Minimize the following functions to a minimum sum of product using rules of Boolean algebra:

a- F(X, Y, Z) = ∑m(0,2,4,6)

b- F(X, Y, Z) = ∑m(1,2,3,7)

c- F(X, Y, Z) = ∑m(1,2,3,6,7)

d- F(W,X,Y,Z) = Σ(0,4,5,6,7,8,14,15)

Then draw them using AND, OR, inverter gates.

4) Minimize the following functions to a minimum product of sums using rules of Boolean algebra:

a- WX(Z+XZ’) + X(Y+Y’WZ)

b- (X’Y + XY’)(WX+W’X’)+(WY)’

5) Analyze the following circuit and express g as a minimal sum of product expression.