American University of Beirut

Department of Electrical and Computer Engineering

EECE 320 – Digital Systems Design

Assignment 1

Due 7-10-11at 11am in class

Suggested problems: Solve the drill problems of chapter 2.

Problem 1: Complete the following table. Numbers are signed except when they are listed in the Unsigned Binary column. Use the necessary number of bits.

| Decimal | Octal | Hexadecimal | Unsigned Binary | Signed-Magnitude | Signed 1’s complement | Signed 2’s complement |
| --- | --- | --- | --- | --- | --- | --- |
| 37.75 |  |  |  |  |  |  |
| -28.875 |  |  |  |  |  |  |
|  |  | C8 |  |  |  |  |
|  |  | 58C.4 |  |  |  |  |
|  |  |  | 10110101 |  |  |  |
|  |  |  |  | 11010100 |  |  |
|  |  |  | 01010101 |  |  |  |
|  |  |  |  |  | 10010.0111 |  |
|  |  |  |  |  |  | 1110.011 |

Problem 2: Find the 9’s complement of the decimal number 4653.

.prove that 7218 – 4653 can be found as 7218 plus the 10’s complement of 4653.

Problem 3:  Assuming those are signed numbers written in 2’s complement compute using 2’s complement arithmetic:

- 010010 – 010101

- 1101 – 100110

Problem 4: Add the following Hexadecimal numbers:

4EB3F7E + 3F5FD4D

Problem 5: Add the following BCD numbers and verify your result by performing the corresponding decimal operation (hint: if the sum of two BCD digits is larger than 9 add 6 to this sum to get the result as a BCD digit):

1001+0110;	0110+0111;	1001+1001;	0101 1001 + 1001 0110