| H. AKKARY | DEPT. OF ELECTRICAL AND COMPUTER ENGINEERING | Nov 18, 2009 |
| --- | --- | --- |
|  | AMERICAN UNIVERSITY OF BEIRUT |  |
|  | EECE320 – Digital Systems Design |  |
|  | QUIZ I – FALL 2009 |  |
| NAME: _____________________________________________________ |  |  |
| ID: ______________________________________________ |  |  |

INSTRUCTIONS:

| Problem | Total Points | Earned Points |
| --- | --- | --- |
| 1 | 28 |  |
| 2 | 12 |  |
| 3 | 30 |  |
| 4 | 30 |  |
|  | 100 |  |

Problem 1: Number Systems [28 points Total]:

- [8 points] Perform the following number systems conversion

- 1100101001101 = ?16

- 101.0112 = ?10

- 1100101001101 =?4

- 20110= ?2

- [4 points] Write -5010  in 1’s complement

- [4 points] Write -7110 in 2’s complement

- [2 points] Add the following numbers: 10111012 + 11000112

- [2 points] Subtract the following numbers: 11000112 – 01101012

- [4 points] Subtract using 2’s complement, as typically done in a computer hardware using 8-bit adders.

- 1210 – 710

- Assuming the hardware has one 8-bit adder. How many add operations are needed to do the subtraction.

- [4 points] Indicate whether an overflow occurs when adding the following 8-bit 2’s complement

- 110101002 + 111010112

- 101110112 + 100001112

Problem 2: Boolean Algebra [12 Points Total]

- [3 points] Using variables Nerd, Designer, Failure and Studied, write a Boolean expression that is 1 for successful designers who never studied and for nerds who studied all the time.

- [3 points Prove the following consensus theorem using perfect induction:

xy + x’z + yz = xy + x’z

- [3 points] Write the canonical sum for F1 and the canonical product for F2.

F1 = Sw,x,y,z(1,4,7,15),  F2 = Pw,x,y,z(0,4,8,12)

- [3 points] Draw a truth table for each of F1 and F2.

Problem 3: Combinational Logic Design [30 Points Total]

- [10 points ] Design a minimum circuit that can subtract two 2-bit binary numbers, and draw its logic diagram.

- [10 points] Design a minimum combinational circuit that detects if a 16-bit binary number is odd and draw its logic diagram.

- Mathematicians do not consider 1 to be a prime number.

- [3 points] Write the minterm list, the canonical sum of a function that detects if a 3-bit binary number is prime or not.

- [7 points] Minimize the function using Karnaugh map and then draw its block diagram.

Problem 4: Logic Minimization [30 Points Total]

- [10 points] Using Karnaugh maps, minimize the function F = Sw,x,y,z(1,4,5,6,7,9,14,15)

- [10 points] Use DeMorgan’s theorem and sum of product function minimization with Karnaugh maps to minimize the function F = Pw,x,y,z(1,4,5,6,11,12,13,14).

- [10 points] Use Karnaugh maps to minimize Fw,x,y,z(1,3,5,14) + d(8, 15).

# Text boxes

- THE EXAM IS CLOSED BOOK/CLOSED NOTES.

- THE DURATION IS 2.0 HOURS.

- CALCULATORS ARE NOT ALLOWED.

- CELL PHONES ARE NOT ALLOWED IN THE EXAMINATION ROOM.

- WRITE YOUR NAME AND ID NUMBER IN THE SPACE PROVIDED ABOVE.

- PROVIDE YOUR ANSWERS IN THE SPACE PROVIDED ON THE QUESTION SHEET.

- THE SCRATCH BOOKLET WILL NOT BE CONSIDERED IN GRADING.

- BE AS NEAT AND CLEAR AS POSSIBLE.