| H. AKKARY | DEPT. OF ELECTRICAL AND COMPUTER ENGINEERING | Jan 11, 2010 |
| --- | --- | --- |
|  | AMERICAN UNIVERSITY OF BEIRUT |  |
|  | EECE320 – Digital Systems Design |  |
|  | QUIZ II – FALL 2009 |  |
| NAME: _____________________________________________________ |  |  |
| ID: ______________________________________________ |  |  |

INSTRUCTIONS:

| Problem | Total Points | Earned Points |
| --- | --- | --- |
| 1 | 10 |  |
| 2 | 10 |  |
| 3 | 10 |  |
| 4 | 10 |  |
| 5 | 10 |  |
| 6 | 10 |  |
| 7 | 10 |  |
| 8 | 10 |  |
| 9 | 10 |  |
| 10 | 10 |  |
|  | 100 |  |

- Use a 1 to 8 de-multiplexer to build a 3-input decoder.

- Use the decoder from problem 1 and OR gates to implement a 3-bit prime number detector circuit. Reminder: the number 1 is not prime.

- A) Draw a tri-state buffer and explain how it works.

B) Draw a 1-bit transceiver and its control and explain how it works.

- Consider a 4x1 PLA with 4 product terms.

Minimize and implement using this PLA the sum of product function Sw,x,y,z(1,3,4,5,9,11,12,13,14,15)

- Let A and B be two 8-bit positive binary numbers. Use an iterative circuit to design a magnitude comparator that outputs a 1 when A is larger or equal to B.

- Show how to build a D flip-flop using a T flip-flop with enable and combinational logic.

- Explain the concept of metastability in S-R flip-flop. Give an example.

- Show how to build an edge-triggered S-R flip-flop using an edge-triggered D flip-flop and combinational logic. Assume that a combination of S=1 and R=1, does not change the state.

- Design a synchronous state machine with two inputs x and y. The output z is to be ‘1 when the inputs x and y are the same a multiple of 3 times.

- Design a synchronous state machine with one input signal x and one output signal y. The state machine is to detect a sequence of ‘1100 on input x and to output a ‘1 for one cycle on y when the sequence is detected.

# Text boxes

- THE EXAM IS CLOSED BOOK/CLOSED NOTES.

- THE DURATION IS 2.0 HOURS.

- CALCULATORS ARE NOT ALLOWED.

- CELL PHONES ARE NOT ALLOWED IN THE EXAMINATION ROOM.

- WRITE YOUR NAME AND ID NUMBER IN THE SPACE PROVIDED ABOVE.

- PROVIDE YOUR ANSWERS IN THE SPACE PROVIDED ON THE QUESTION SHEET.

- THE SCRATCH BOOKLET WILL NOT BE CONSIDERED IN GRADING.

- BE AS NEAT AND CLEAR AS POSSIBLE.