American University of Beirut

Department of Electrical and Computer Engineering

EECE 320 – Digital Systems Design

Assignment 1

Suggested problems: Solve the drill problems of chapter 2.

Problem 1: Complete the following table

| Decimal | Octal | Hexadecimal | Unsigned Binary | Signed-Magnitude | Signed 1’s complement | Signed 2’s complement |
| --- | --- | --- | --- | --- | --- | --- |
| 18.75 | 22.3 | 12.3 | 10010.11 | 010010.11 | 001101.11 | 001110.11 |
| -12.875 | -14.7 | -C.7 | 1100.111 | 11100.111 | 10011.111 | 10100.111 |
| 63.26 | 76.32 | 3E.1A | 111110.11010 | 0111110.11010 | 0000001.11010 | 0000010.11010 |
| 910.3 | 1616.3 | 38E.3 | 1110001110.0011 | 01110001110.0011 | 00001110001.0011 | 0001110010.0011 |
| 202 | 312 | 0CA | 11001010 | 011001010 | 000110101 | 000110110 |
| -74 | -112 | -04A | 1001010 | 11001010 | 10110101 | 10110110 |
| 41 | 051 | 029 | 0101001 | 00101001 | 01010110 | 01010111 |
| -5.375 | -05.3 | -5.3 | 0101.011 | 10101.011 | 11010.011 |  |
| -5.3 | -5.3 | -5.3 | 101.11 | 1101.11 | 1010.11 | 1011.11 |

Problem 2: Find the 9’s complement of the decimal number 678 546 900.

Find the 16’s complement of the hexadecimal number AB45.

_ 9’s complement of 678 546 900: 999999999-678546900 = 321453099.

_ 15’s complement of AB45: 54BA (By substracting 15 from each digit).

16’s complement of AB45: 15’s complement+1 = 54BA+1 = 54BB.

Problem 3: Perform subtraction directly first then using the 2’s complement of the subtrahend for the following numbers:

- 110010 – 110101

Direct substraction:

110010

- 110101

1 111101 (the following number is in signed 2’s complement)

Using 2’s complement:

2’s complement of 110101 is 001010+1 = 001011.

Performing addition:

110010

+001011

1 11101  (the following number is in signed 2’s complement)

- 1101 – 101000

Direct substraction:

001101

- 101000

1 100101 (the following number is in signed 2’s complement)

Using 2’s complement:

2’s complement of 101000 is 010111+1 = 011000.

Performing addition:

001101

+011000

1 100101 (the following number is in signed 2’s complement)

Problem 4: Add the following Hexadecimal numbers:

4AB3F7C + 3F6FE4D.

4 (10) (11)   3    (15)   7  (12)

+ 3 (15)  6    (15)  (14)   7  (13)

8 (10)  2      4     (13) (15) 9

Therefore 4AB3F7C + 3F6FE4D = 8A24DF9

Problem 5: Add the following BCD numbers and verify your result by performing the corresponding decimal operation:

1000+0101;	0011+0110;	1001+1001;	0010 1000 + 1000 1000.

1)In Binary: 1000+0101 = 1101.

In Decimal: 1000 = 8.

0101 = 5.

1101 = 13.

And 8 + 5 = 13.

2) In Binary: 0011+0110 = 1001.

In Decimal: 0011 = 3.

0110 = 6.

1001 = 9.

And 6 + 3 = 9 .

3) In Binary: 0011+0110 = 1001.

In Decimal: 0011 = 3.

0110 = 6.

1001 = 9.

And 6 + 3 = 9

4) In Binary: 1001+1001 = 10010.

In Decimal: 1001 = 9.

1001 = 9.

10010 = 18.

And 9 + 9  = 18.

5) In Binary: 00101000 + 10001000 = 10110000.

In Decimal:  00101000 = 40.

10001000 = 136.

10110000 = 176.

And 40 + 136 = 176

Problem 6: Using the ASCII table, convert the following message to binary.

Good Night!

G = 01000111.

o  = 01101111.

d  = 01100100.

N = 01001110.

i   = 01101001.

g  = 01100111.

h  = 01101000.

t   = 01110100.

Therefore

Good Night  ==

01000111 0110111101101111 01100100 0100111001101001011001110110100001110100