EECE 290

Quiz 3, Apr 16, 2016

4% (Primal Question)

- Determine vC(t), t ( 0+, assuming vSRC(t) = ((t) V and the

capacitor to be initially uncharged.

Solution:	If the impulse is K((t) V, it will cause a current

impulse of K((t) A through the capacitor, depositing a charge of

K C on the capacitor and resulting in vC(0+) = K V; ( = 0.5 s, so that V, t is in s.

Version 1: K = 1, = V

Version 2: K = 2, = 2V

Version 3: K = 3, = 3V

Version 4: K = 4, = 4V

Version 5: K = 5, = 5V.

4% (Primal Question)

- The switch is closed at t = 0, with the 2 (F capacitor initially charged to V0 = 2 V, and the 6 (F capacitor uncharged. Determine the common voltage across the capacitors at t = 0+,

and the strength of the impulse that flows.

Solution: The initial capacitor charge is 2V0 (C, and the final voltage is 2V0/8 = V0/4 V. The charge on the 6 (F capacitor is 1.5V0 C, which is the strength of the current impulse.

Version 1: V0 = 2 V, v(0+) = V0/4 = 0.5 V, q = 1.5V0 = 3 C

Version 2: V0 = 4 V, v(0+) = V0/4 = 1 V, q = 1.5V0 = 6 C

Version 3: V0 = 6 V, v(0+) = V0/4 = 1.5 V, q = 1.5V0 = 9 C

Version 4: V0 = 8 V, v(0+) = V0/4 = 2 V, q = 1.5V0 = 12 C

Version 5: V0 = 10 V, v(0+) = V0/4 = 2.5 V, q = 1.5V0 = 15 C.

4% (Primal Question)

C.	Determine the maximum value of the convolution integral when the two pulses are convolved together, assuming A = 1.

Solution: The maximum area under the product is 2A×2 = 4A.

Version 1: A = 1, ym = 4A = 4

Version 2: A = 1.5, ym = 4A = 6

Version 3: A = 2, ym = 4A = 8

Version 4: A = 2.5, ym = 4A = 10

Version 5: A = 3, ym = 4A = 12.

4% (Primal Question)

D.	Derive the ILT of .

Solution: The PFE of  is . The ILT is A(1 – cost)u(t).

Version 1: A = 1, ILT = A(1 – cost) = (1 – cost)u(t)

Version 2: A = 2, ILT = A(1 – cost) = 2(1 – cost)u(t)

Version 3: A = 3, ILT = A(1 – cost) = 3(1 – cost)u(t)

Version 4: A = 4, ILT = A(1 – cost) = 4(1 – cost)u(t)

Version 5: A = 5, ILT = A(1 – cost) = 5(1 – cost)u(t).

4%

1.	Determine iL(0+), assuming IL0 = 2 A and

K = 1 Vs.

Solution: The current source in parallel with the ideal voltage source is redundant. The impulse appears across the inductor establishing a flux linkage of K Wb-T and causing a current of K/1 = K A at t = 0+. This adds to IL0, so that iL(0+) = K + 2 A. For t ( 0+, the voltage source acts as a short circuit, thereby diverting the current source.

Version 1: K = 1 Vs, iL(0+) = K + 2 = 3 A

Version 2: K = 2 Vs, iL(0+) = K + 2 = 4 A

Version 3: K = 3 Vs, iL(0+) = K + 2 = 5 A

Version 4: K = 4 Vs, iL(0+) = K + 2 = 6 A

Version 5: K = 5 Vs, iL(0+) = K + 2 = 7 A.

4%

2.	Determine iR(t), t ( 0+, assuming at t = 0- an initial

voltage of 5 V across the capacitor and an initial circulating current of 2 A, with K = 1 A.

Solution: When the current step is applied, the current through the inductor is not forced to change. iR(0+) = (K + 2) A. As t ( (, the inductor acts as a short-circuit, so that the source current flows through the short circuit and iR ( 0. ( = 0.5 s, so that  A, t is in s.

Version 1: K = 1 C, =  A, t is in s

Version 2: K = 2 C, =  A, t is in s

Version 3: K = 3 C, =  A, t is in s

Version 4: K = 4 C, =  A, t is in s

Version 5: K = 5 C, =  A, t is in s.

4%

3.	Determine iC(0+), assuming no initial current in the inductor, an initial V0 = 1 V, and K = 1 Vs.

Solution: Initially, the inductor acts as an open circuit, the capacitor voltage is not forced to change at t = 0+, and an initial current of 1 A flows downwards through the resistor. The voltage impulse appears across the inductor, establishing a flux linkage of K Wb-T and causing a current of 2K A to flow through the inductor. It follows that iC(0+) = (2K – 1) A.

Version 1: K = 1 Vs, iC(0+) = (2K – 1)  = 1 A

Version 2: K = 2 Vs, iC(0+) = (2K – 1)  = 3 A

Version 3: K = 3 Vs, iC(0+) = (2K – 1)  = 5 A

Version 4: K = 4 Vs, iC(0+) = (2K – 1)  = 7 A

Version 5: K = 5 Vs, iC(0+) = (2K – 1)  = 9 A.

4%

4.	Determine iR(t), t ( 0+, assuming an initial voltage

V0 = 4 V, and no initial charge in the other two capacitors.

Solution: When the switch is closed, the voltages across the two 1 (F capacitors are forced to become equal, that across the 2 (F is not forced to change because of iR, which is finite. Charge is conserved between the two 1 (F capacitors at t = 0+, so that the voltage across them at t = 0+ is V0/2 V. iR(0+) = (V0/4) A. The equivalent capacitance in series with the resistor is 1 (F, so that ( = 2 (s. Hence,  A, t in (s.

Version 1: V0 = 4 V,  =  A, t in (s

Version 2: V0 = 8 V,  =  A, t in (s

Version 3: V0 = 12 V,  =  A, t in (s

Version 4: V0 = 16 V,  =  A, t in (s

Version 5: V0 = 20 V,  =  A, t in (s.

4%

5.	f(t) is convolved with the impulses (((t + 1) + ((t – 1)). Determine

the value of the convolution integral at t = 0.

Solution: When f(t) is convolved with ((t + 1), it is shifted by 1 unit to the left. Its value at t = 0 is 2. When convolved with ((t – 1), it is shifted by 1 unit to the right. Its value at t = 0 is also 2. Hence y(0) = 4. If the impulses have a strength of K, y(0) = 4K.

Version 1: K = 1, y(0) = 4K = 4

Version 2: K = 1.25, y(0) = 4K = 5

Version 3: K = 1.5, y(0) = 4K = 6

Version 4: K = 1.75, y(0) = 4K = 7

Version 5: K = 2, y(0) = 4K = 8.

4%

6.	Determine the LT of the derivative of f(t), assuming A = 1.

Solution: The derivative of f(t) is a shown. The LT, neglecting values for

t < 0 is: . As a check, the LT of f(t)

is: =

= . Multiplying by s and subtracting A/2, gives , the same as above.

Version 1: A = 1,

Version 2: A = 2,

Version 3: A = 4,

Version 4: A = 6,

Version 5: A = 8, .

20%

7.	Given C1 = 8 F, initially charged to V10 = 6 V, C2 = 6 F, initially charged to V20 = 4 V, and C3 = 3 F, initially charged to V30 = 2 V. The switch is closed at t = 0. Determine the final values of v2 and v3.

Solution: Because of the short circuit by the switch, C2 and C3 discharge independently of C1. The initial charges are q2 = 24 C and q3 = 6 C. The equivalent series capacitor is 2 F and has an initial voltage of 6 V, so that its charge is 12 C. When this capacitor discharges, 12 C flow CCW. When these flow through C2 and C3, q3f =

-6 C, so that v3f = -2 V, and q2f = 12 C, so that v2f = 2 V.

20%

8.	Derive y(t) = f(t)(g(t) for all t.

Solution: When g(t) is folded and shifted, it is seen that:

- For t ( -1, y(t) = 0

- For -1 ( t ( 0, y(t) =  . In terns of the area of the triangle, y(t) = . At the limits of this interval, y(-1) = 0, and y(0) = 1/2.

- For 0 ( t ( 1, y(t) =

= . In terms of areas, the area of the trapezoid is . The area of the

triangle is . Adding these two gives . At the limits of this interval, y(0) = 1/2, and y(1) = -1/2.

- For 1 ( t ( 2, y(t) =. In terms of areas, the area of the trapezoid is . At the limits of this interval, y(1) = -1/2, and y(2) = 0.

- For t ( 2, y(t) = 0.

20%

9.	Given vSRC(t) =  V, with an initial voltage

VC0 = 1 V at t = 0-. (a) Express KCL at the upper node in terms of vSRC(t) and iSRC(t) and take the LT of both sides of the equation (4 grades); (b) derive Isrc(s) as a rational function of s (8 grades); (c) obtain iSRC(t) by ILT (8 grades).

Solution: (a) iSRC = vSRC/1 + 1×dvSRC/dt; taking the LT of both sides: Isrc(s) = Vsrc(s)(s + 1) – 1.

(b)	; substituting for Vsrc(s), Isrc(s) = .

(c)	Taking the ILT, iSRC(t) =  A.