EECE 290

Quiz 2, Mar 19, 2016

4% (Primal Question)

A.	Given the transfer function  for a normalized second-order Butterworth filter. Determine the transfer function of the filter when the frequency is scaled to 10 rad/s.

Solution: Coefficient of s is (0/Q, where Q of the Butterworth filter is . The constant term is term is .

Version 1: (0 = 10 rad/s, H(s) =

Version 2: (0 = 20 rad/s, H(s) =

Version 3: (0 = 30 rad/s, H(s) =

Version 4: (0 = 40 rad/s, H(s) =

Version 5: (0 = 50 rad/s, H(s) = .

4% (Primal Question)

B.	 Enter between the parenthesis (T) or (F) according to whether the statement is true or false, respectively:

(  T  )	The average value of f(t) is 4

(  F  )	The ac component of the FSE of f(t) consists of even harmonic only

(  T  )	The trigonometric terms of the FSE are cosine functions only

(  F  )	The harmonics of the FSE of f(t) attenuate at a rate of approximately 1/n

(Note: 1 grade for each correct answer. No penalty for wrong answers)

4% (Primal Question)

C.	Determine the reactive power absorbed by the inductor

and the capacitor, assuming VSRC(j() = 10(-45( V rms.

Solution: QL = -|VSRC(j()|2BL = -|VSRC(j()|2×[-(1/20)]; QC =

-|VSRC(j()|2BC = -|VSRC(j()|2×[(1/10)].

Version 1: |VSRC(j()| = 10; QL = 100/20 = 5 VAR, QC = -100/10 = -10 VAR

Version 2: |VSRC(j()| = 20; QL = 400/20 = 20 VAR, QC = -400/10 = -40 VAR

Version 3: |VSRC(j()| = 30; QL = 900/20 = 45 VAR, QC = -900/10 = -90 VAR

Version 4: |VSRC(j()| = 40; QL = 1600/20 = 80 VAR, QC = -1600/10 = -160 VAR

Version 5: |VSRC(j()| = 50; QL = 2500/20 = 125 VAR, QC = -2500/10 = -250 VAR

4% (Primal Question)

D.	A source has an open circuit voltage of 10(-140( V rms, a source inductance of 10 mH and a source resistance of 10 ( , the frequency being 400 Hz. Determine the load that will absorb maximum power from this source and the value of this power.

Solution: The source reactance is 2(×400×10-2 = 8(  (. For maximum power transfer, the load resistance should be 10 ( and the reactance should be -8( (, which gives a capacitance of -1/(8(×800() ( 15.8 (F. The power delivered is PL = |VSRC|2/(4*10) =

Version 1: |VSRC| = 10; PL = 100/40 = 2.5 W

Version 2: |VSRC| = 8; PL = 64/40 = 1.6 W

Version 3: |VSRC| = 6; PL = 36/40 = 0.9 W

Version 4: |VSRC| = 5; PL = 25/40 = 0.625 W

Version 5: |VSRC| = 4; PL = 16/40 = 0.4 W.

4%

1.	A highpass 4th order Butterworth filter has a passband gain of 10 and a 3-dB cutoff frequency of 10 kHz. Determine the frequency at which the gain is 10-6.

- Hz

- Hz

- Hz

- Hz

- 177.8 Hz

Solution: For a 4th order highpass Butterworth filter of a passband gain of 10, . The frequency fx at which the gain is A×10-6 is small compared to fch if A is relatively small. Hence, (fch/fx) >> 1, so that , or = , or, = 177.8 Hz if A = 1. Alternatively, fx will lie on the LF asymptote, whose slope is 80 dB/dec. The gain of 10-6 is 10-7 below the passband gain, which corresponds to -140 dB. This is 140/80 = 7/4 decades less than 10 kHz, which gives fX = 104×10-7/4 = 177.8 Hz

Version 1: A = 1,  = 177.8 Hz

Version 2: A = 2,  = 211.5 Hz

Version 3: A = 3,  = 234.0 Hz

Version 4: A = 4,  = 251.5 Hz

Version 5: A = 5,  = 265.9 Hz

4%

2.	Determine the type of response VO(j()/VSRC(j().

- V

- Lowpass

- V

- V

- V

Solution: Let the RC combination be denoted by Zf and the RL combination be denoted by Zr.

Since the op amp is ideal, the voltage across the RL combination is VN = VSRC, because of the virtual short circuit. The current through Zr is VSRC/Zr. It follows that VO = VN – VSRC + VSRCZf/Zr = VSRCZf/Zr, where Zf = R/(1 + j(CR) = 1/(s + 1), and Zr = (R + j(L) = (s + 1), so that . The response is second-order lowpass.

4%

3.	f1(t) and f2(t) are, respectively, the square

and triangular waveforms shown, each having an amplitude A and zero average value. Determine the component of (f1(t) + f2(t)) having a frequency of 3( /2 rad/s, assuming

A = 1.

- -0.42cos1.5(t

Solution: The period of f1(t) is 4 s, so (01 = 2( /4 = ( /2. The period of f2(t) is 2 s, so (02 = 2(/2 = (. Both waveforms are quarter-wave symmetric and have odd harmonics only, so that the harmonics of f1(t) are 3( /2, 5( /2, etc. The harmonics of f2(t) are 3( , 5( , etc. The FSE of the sum of the two FSEs will have a component at a frequency of 3( /2 due to the third harmonic of f1(t) only. Hence, . It follows that the component of frequency 3( /2 is .

Version 1: A = 1, a3 = -4/3( = -0.42cos1.5(t

Version 2: A = 2, a3 = -8/3( = -0.85cos1.5(t

Version 3: A = 3, a3 = -12/3( = -1.27cos1.5(t

Version 4: A = 4, a3 = -16/3( = -1.70cos1.5(t

Version 5: A = 5, a3 = -20/3( = -2.12cos1.5(t.

4%

4.	f(t) is a periodic waveform of period 4 s, its ac component

is quarter-wave symmetric, with f(t) = (5 + A) + kt2, 0 < t ( 1, where A = 1 and k is such that the rms value of f(t) is 8.

Determine the rms value of the ac component of |f(t)| when delayed by 1 s.

- 5.92

Solution: The required rms value is the same as that of the ac component of f(t). The average value of f(t) is A. Hence, , so that

Version 1: A = 1, f(t)rms = 6;

Version 2: A = 2, f(t)rms = 6;

Version 3: A = 3, f(t)rms = 6;

Version 4: A = 4, f(t)rms = 7;

Version 5: A = 5, f(t)rms = 8, 6.24.

4%

5.	Load 1 absorbs a complex power of  VA, whereas load 2 absorbs a complex power of

VA. Determine XL, assuming ISRC = 0.25(-30( A. Note that the other circuit parameters need not be specified.

- (

- (

- 400 (

- (

- (

Solution: The total complex power delivered by the source = (10 + j10) + (5 – j5) = 15 + j5 VA.  = 250/|ISRC|2; reactive power absorbed by XL is 10 = 250/(XL|ISRC|2); hence, XL = 25/|ISRC|2.

Version 1: |ISRC| = 0.25, XL = 25/|ISRC|2 = 25/0.0625 = 400 (

Version 2: |ISRC| = 0.5, XL = 25/|ISRC|2 = 25/0.25 = 100 (

Version 3: |ISRC| = 1.25, XL = 25/|ISRC|2 = 25/1.5625 = 16 (

Version 4: |ISRC| = 2, XL = 25/|ISRC|2 = 25/4 = 6.25 (

Version 5: |ISRC| = 2.5, XL = 25/|ISRC|2 = 25/6.25 = 4 (

4%

6.	If XL can be varied between -30 and -50 (, determine the maximum power that can be delivered to the 10 ( resistor, assuming VSRC = 10(30( V rms.

- 0.8 W

Solution: The voltage source and the series impedance are transformed to a current source ISRC in parallel with an admittance Ysrc, where ISRC =  A, |ISRC| =  A rms, , so that Gsrc = 1/40 S and Bsrc = -1/40 S. For maximum power transfer, BL = 1/40 S, or XL = -40 (, which is within the given range of XL. The circuit reduces to ISRC in parallel with 40 ( and 10 (. The current in the 10 ( resistor is ISRC×40/50 = 0.8ISRC. The power absorbed by the 10 ( resistor is PL = 0.64|ISRC|2×10 =

Version 1: |VSRC| = 10; PL = |VSRC|2/125 = 100/125 = 0.8 W

Version 2: |VSRC| = 15; PL = |VSRC|2/125 = 225/125 = 1.8 W

Version 3: |VSRC| = 20; PL = |VSRC|2/125 = 400/125 = 3.2 W

Version 4: |VSRC| = 25; PL = |VSRC|2/125 = 625/125 = 5 W

Version 5: |VSRC| = 30; PL = |VSRC|2/125 = 900/125 = 7.2 W.

20%

7.	(a)	Derive the transfer function

VO(j()/VI(j() (12 grades).

(b)	Characterize the response (3 grades).

(c)	Determine the maximum gain

(2 grades), the minimum

gain (3 grades), both in dB, and the

frequencies at which they occur.

Solution: (a) The lower 3-dB cutoff frequency Is  = 125 rad/s; the upper 3-dB cutoff frequency is  krad/s. The transfer function is .

(b) The response is a combination of second-order bandpass and second-order bandstop responses.

(c) The maximum gain is 10, or 20 dB, and occurs as ( ( 0, or, ( ( (. The minimum gain is 10×250/100125 ( 0.025 ( 20log10(0.025) = -32 dB

20%

8.	(a) Derive the first three terms of the FSE of f(t), where f(t) =

4 + sin 2t, -(/2 < t < (/2 and f(t) = -4 + sin 2t, -( ( t < -(/2 and

(/2 < t ( ( (16 grades); (b) determine these terms when f(t) is advanced by a quarter period (4 grades).

Solution: (a) f(t) is neither odd nor even, is not half-wave

symmetric, and is of zero average. It is the sum of sin2t and an even square wave of amplitude 4, zero average,

and period 2(, or (0 = 1 rad/s. The square wave is quarter-wave symmetric so it consists of odd cosine terms only.  . The fundamental is , and the third harmonic is . The sinusoidal function is its own FSE, so that the first three terms of the FSE of f(t) are:  + sin2t .

(b) If the function is advanced by a quarter period, the phase angle is increased by n(0ta, where (0 = 1 rad/s, and ta = (/2 s. The FSE becomes  + sin(2t + () = – sin2t . The function becomes odd.

20%

9.	A load RL + jXL is connected between terminals ‘ab’,

where RL can be varies between 0 and 10 (

and XL can be varied between (5 (.

Determine: (a) the values of RL and XL

that result in maximum power dissipated in RL

(15 grades); (b) the complex power absorbed by the load under these conditions (5 grades).

Solution: The parallel impedance of the resistor and capacitor is

-j8(1 + j2) = 16 – j8 (; VTh = 5(16 – j8) = 80 – j40 V rms. The total source impedance is 16 – j8 + 4 + j18 = 20 + j10 (.

(a) XL that maximizes power transfer is that which minimizes the total reactance. Hence, XL = -5 (. RL for maximum power transfer = 20.62 (. Hence, RL = 10 ( should be used. The circuit becomes as shown. |I|2 =

A2. The real power dissipated in RL is |I|2RL = 86.5 W and the reactive power absorbed by XL is -5|I|2 = -43.2 VAR. Hence, SL = 86.5 – j43.2 VA.