EECE 290

Quiz 1, February 20, 2016

4% (Primal Question)

A.	Determine VO assuming VSRC = 1 V.

Solution: The two 1 k( resistors in series with the op amp inputs are redundant since they do not carry any current. The 2 k( resistors across

VSRC and the op amp output are redundant since they are connected in parallel with ideal voltage sources. The circuit reduces to a noninverting configuration having Rf = 2 k( and Rr = 1 k(. It follows that VO = (1 + Rf/Rr)VSRC = 3VSRC V.

Version 1: VSRC = 1 V, VO = 3 V

Version 2: VSRC = 1.5 V, VO = 4.5 V

Version 3: VSRC = 2 V, VO = 6 V

Version 4: VSRC = 2.5 V, VO = 7.5 V

Version 5: VSRC = 3 V, VO = 9 V

4% (Primal Question)

B.	Determine VO assuming VSRC = 1 V.

Solution: The 1 k( resistor in series with the noninverting input is redundant since it does not carry any current. The

2 k( resistor connected between the inverting input and ground is redundant since this input is a virtual ground. The 2 k( resistor at the op amp output is redundant since it is connected in parallel with an ideal voltage source. The circuit reduces to an inverting configuration having Rf = 2 k( and Rr = 1 k(. It follows that VO = -Rf/RrVSRC = -2VSRC V,

Version 1: VSRC = 1 V, VO = -2 V

Version 2: VSRC = 1.5 V, VO = -3 V

Version 3: VSRC = 2 V, VO = -4 V

Version 4: VSRC = 2.5 V, VO = -5 V

Version 5: VSRC = 3 V, VO = -6 V

4% (Primal Question)

C.	Sketch vO(t) when vSRC(t) is the triangular waveform shown, assuming A = 1 V,

Solution: ir(t) = vSRC(t)/1 = vSRC(t) A; vO(t) = -1(dVSRC(t)/dt

is the square waveform shown of amplitude A V/s.

Version 1: A = 1 V

Version 2: A = 2 V

Version 3: A = 3 V

Version 4: A = 4 V

Version 5: A = 5 V

4% (Primal Question)

D.	Determine the type of response VO(j()/ISRC(j(), its maximum magnitude, and the Q, assuming R = 10 (.

Solution: The response is bandpass. The maximum magnitude is at resonance, when ISRC(j() flows through R, so that the maximum response is R (;  = 1000 rad/s; Qp = (0CR = 103(10-3R = R.

Version 1: R = 10 (; maximum response is 10 (; Q = 10

Version 2: R = 20 (; maximum response is 20 (; Q = 20

Version 3: R = 30 (; maximum response is 30 (; Q = 30

Version 4: R = 40 (; maximum response is 40 (; Q = 40

Version 5: R = 50 (; maximum response is 50 (; Q = 50

4%

1.	Determine VO, assuming VSRC = 6 V.

- V

- V

- V

- 15 V

- V

Solution: VP = (2/3)VSRC; VN = VP; the current flowing

through the 1 k( resistor to ground is (2/3)VSRC mA. VO = (2/3)VSRC +

3(2/3)VSRC = (8/3)VSRC = 16 V. If VSRC ( 6 V, the op amp is in positive saturation, so that

VO = 15 V.

Version 1: VSRC = 6 V, VO = 15 V

Version 2: VSRC = 7 V, VO = 15 V

Version 3: VSRC = 8 V, VO = 15 V

Version 4: VSRC = 9 V, VO = 15 V

Version 5: VSRC = 10 V, VO = 15 V

4%

2.	Determine the maximum magnitude of VO and the

phase angle at this magnitude, assuming VSRC = 1(0( V.

- V

- 1 V, 180(

- V

- V

- V

Solution: Because of the virtual short circuit, maximum

current occurs when the inductor or the capacitor acts as a

short circuit, and is equal to VSRC/2 mA. This current flows through the 1 k( resistors, giving VO = -2(VSRC/2) = -VSRC V.

Version 1: VSRC = 1 V, VO = 1 V, 180(

Version 2: VSRC = 2 V, VO = 2 V, 180(

Version 3: VSRC = 3 V, VO = 3 V, 180(

Version 4: VSRC = 4 V, VO = 4 V, 180(

Version 5: VSRC = 5 V, VO = 5 V, 180(

4%

3.	A lowpass, first-order transfer function H1(j() has a maximum gain in the passband of -2 dB and a corner frequency of 50 kHz. Another lowpass, first-order transfer function H2(j() has a magnitude that is 8 times that of H1(j() and a corner frequency of 1 kHz. Determine |H1(j()H2(j()| in dB when it falls 3 dB below its maximum value at low frequencies.

- dB

- dB

- 11 dB

- dB

- dB

Solution: The maximum value of 20log10|H1(j()| is -A dB. The maximum value of 20log10|H2(j()| is -A + 20log10(8) = -A + 18 dB. The maximum value of 20log10|H1(j()H2(j()| is -A + 18 – A = (18 – 2A). At a level -3 dB below this, the gain is (15 – 2A) dB.

Version 1: A = 2 dB, gain = (15 – 2A) = 11 dB

Version 2: A = 3 dB, gain = (15 – 2A) = 9 dB

Version 3: A = 4 dB, gain = (15 – 2A) = 7 dB

Version 4: A = 6 dB, gain = (15 – 2A) = 3 dB

Version 5: A = 7 dB, gain = (15 – 2A) = 1 dB.

4%

4.	Determine the frequency at which the high-frequency asymptote of the response VO(j()/VSRC(j() crosses the

0 dB line, assuming L = 1 mH.

- 10 krad/s

- krad/s

- krad/s

- krad/s

- krad/s

Solution: At high frequencies, the inductive reactance dominates. |I| = |VSRC(j()|/(L; IVO(j()| = 10|I| = 10|VSRC(j()|/(L; the high-frequency asymptote is |VO(j()/VSRC(j()| = 10/(L, or, 20log10|VO(j()/VSRC(j()| = 20log10(10/(L); this is zero at (L = 10, or ( = 10/L

Version 1: L = 1 mH; ( = 10/L = 10 krad/s

Version 2: L = 2 mH; ( = 10/L = 5 krad/s

Version 3: L = 4 mH; ( = 10/L = 2.5 krad/s

Version 4: L = 5 mH; ( = 10/L = 2 krad/s

Version 5: L = 8 mH; ( = 10/L = 1.25 krad/s.

4%

5.	Determine the 3-dB bandwidth of the response

VO(j()/ISRC(j(), assuming ( = 1.

- 5 rad/s

Solution: BW = (0/Q = (0/((0Leff/Reff) = Reff/Leff . The current through the source in the direction of a voltage drop is IO(j() = VO(j()/10; the value of the dependent source is (j0.3( + ()10IO(j() = (j3( + 10()IO(j(). The dependent source is equivalent to (j3( + 10(), that is, to an inductance of 3 H and a resistance of 10( (. Hence, Leff = 4 H and Reff = 10(( + 1) (, so that BW = 2.5(( + 1) rad/s.

Version 1: ( = 1, BW = 2.5(( + 1) = 5 rad/s

Version 2: ( = 2, BW = 2.5(( + 1) = 7.5 rad/s

Version 3: ( = 3, BW = 2.5(( + 1) = 10 rad/s

Version 4: ( = 4, BW = 2.5(( + 1) = 12.5 rad/s

Version 5: ( = 5, BW = 2.5(( + 1) = 15 rad/s.

4%

6.	Given the transfer function  . Determine Q if the product of the two 3-dB cutoff frequencies is 106 (rad/s)2.

- 10

Solution: BW = 100 rad/s; ;

Version 1: (c1(c2 = 106; = 103/100 = 10

Version 2: (c1(c2 = 4(106; = 2(103/100 = 20

Version 3: (c1(c2 = 9(106; = 3(103/100 = 30

Version 4: (c1(c2 = 16(106; = 4(103/100 = 40

Version 5: (c1(c2 = 25(106; = 5(103/100 = 50.

20%

7.	Determine VO.

Solution: VP = VN = 2(3||6) =

2(2 = 4 V. A current

of 4 mA flows

in the 1 k(

resistor

towards ground.

The current in

The 2 k(

resistor is

3 mA. It

Follows that

VO = 2(3 + 4 = 10 V.

20%

8.	(a)	Show that the response VO(j()/VSRC(j() is the product of

a first-order lowpass response and a first-order

highpass response (9 grades).

(b)	Choose Rf and Cf so that the

two first-order responses

have the same 3-dB

cutoff frequency, and the

maximum magnitude of the overall

response is 0 dB, assuming R = 2 k( and C = 0.5 (F (8 grades).

(c)	Specify the Q of the overall response (3 grades)

Solution:	(a)	The two 2R resistors are effectively in

parallel, the voltage across them being =

Hence,

. The parallel

impedance of Rf and Cf is Rf/(1 + sCfRf). It follows that H(s) =

, which is the product of a first-order lowpass

response and a first-order highpass response.

(b)	If the two first-order responses have the same cutoff frequency (c, H(s) =

. Multiplying the numerator and denominator by , ; to have a unity magnitude of gain, Rf = 4R = 8 k(. The time constant CR = 0.5(10-6(2(103 = 10-3 s. Hence Cf = 10-3/(8(103) ( 0.125 (F.

(c)	The coefficient of s in the denominator in standard form is (c/Q. It follows that Q = 0.5.

20%

9.	(a)	Determine R so that Q = 10, assuming

C = 75 nF (7 grades).

(b)	Derive the transfer function IO(j()/ISRC(j() (8 grades).

(c)	Characterize the response in terms of the basic responses of second-order circuits (2 grades).

(d)	Determine the gain in dB as ( ( 0 and at ( = (0 (1 grade and 2 grades).

Solution:	(a)	Norton’s equivalent circuit of the capacitive

bridge and current source is first determined.

The current source divides into ISRC(j()/3 through C and 2ISRC(j()/3 through 2C. On short circuit, it is seen that IN = ISRC(j()/3. The capacitance

looking into the capacitive bridge,

with the current source

replaced by an open circuit is

twice C in series with 2C, which is 4C/3

= 100 nF. The circuit becomes the parallel circuit shown. =  rad/s;  k(.

(b)	In terms of admittances,  =

.

(c)	The response is seen to be the sum of a bandpass and a lowpass response.

(d)	As s ( 0, H(j() = 1/3, 20log10(1/3) = -9.54 dB. At ( = (0, s2 = -1010, and H(j(0) = ; 20log10|H(j(0)| =  = 10.5 dB.