EECE 290

Quiz 1, February 22, 2014

4% (Primal Question)

A.	Determine VO, assuming VSRC = 1 V.

Solution: For the noninverting configuration,  = 3, or VO = 3VSRC.

Version 1: VSRC = 1 V, VO = 3 V

Version 2: VSRC = 2 V, VO = 6 V

Version 3: VSRC = 3 V, VO = 9 V

Version 4: VSRC = 4 V, VO = 12 V

Version 5: VSRC = 5 V, VO = 15 V.

4% (Primal Question)

B.	Determine VO, assuming VSRC = 1 V.

Solution: , or VO = -0.5VSRC.

Version 1: VSRC = 1 V, VO = -0.5 V

Version 2: VSRC = 2 V, VO = -1 V

Version 3: VSRC = 3 V, VO = -1.5 V

Version 4: VSRC = 4 V, VO = -2 V

Version 5: VSRC = 5 V, VO = -2.5 V.

4% (Primal Question)

C.	(a) Derive the transfer function VR(j()/VSRC(j() in terms of (, R and C; (b) determine the 3-dB cutoff frequency, assuming C = 0.1 (F.

Solution: 	(a) ;

(b) 3-dB cutoff frequency: (ch = krad/s, C in (F.

Version 1: C = 0.1 (F, (ch = 1/C = 10 krad/s

Version 2: C = 0.2 (F, (ch = 1/C = 5 krad/s

Version 3: C = 0.25 (F, (ch = 1/C = 4 krad/s

Version 4: C = 0.4 (F, (ch = 1/C = 2.5 krad/s

Version 5: C = 0.5 (F, (ch = 1/C = 2 krad/s.

4% (Primal Question)

D.	Determine the 3-dB bandwidth of the response VR(j()/VSRC(j(), assuming R = 1 k(.

Solution: BW krad/s, where R is in k(.

Version 1: R = 1 k(, BW = 10R = 10 krad/s

Version 2: R = 1.5 k(, BW = 10R = 15 krad/s

Version 3: R = 2 k(, BW = 10R = 20 krad/s

Version 4: R = 2.5 k(, BW = 10R = 25 krad/s

Version 5: R = 3 k(, BW = 10R = 30 krad/s.

4%

1.	Determine VO assuming VSRC = 1 V, and an ideal op amp.

- 5 V

- -2.5 V

- 2.5 V

- -5 V

- -10 V

Solution: No current flows through the 10 k( resistor connected to the noninverting terminal. This terminal is therefore at a ground voltage of zero V, and the inverting terminal is a virtual ground.

The current through the 10 k( resistor connected to this terminal

is VSRC/10 mA. No current flows through the 50 k( resistor connected between the inverting terminal and ground. The VSRC/10 mA current flows through the 50 k( resistor, resulting in VO = -50VSRC/10 =

-5VSRC V.

Version 1: VSRC = 1 V, VO = -5VSRC = -5 V

Version 2: VSRC = 1.2 V, VO = -5VSRC = -6 V

Version 3: VSRC = 1.4 V, VO = -5VSRC = -7 V

Version 4: VSRC = 1.6 V, VO = -5VSRC = -8 V

Version 5: VSRC = 1.8 V, VO = -5VSRC = -9 V.

4%

2.	Determine IS assuming VSRC = 2 V, and an ideal op amp.

- -4 mA

- -8 mA

- 8 mA

- 4 mA

- 0

Solution: Because of the virtual short circuit, the voltage drop from the output terminal of the op amp to its noninverting terminal is 5 V. The current through the 1 k( resistor connecting these terminals is 5 mA. This current flows through the 2 k( resistor to ground, resulting in a voltage of 10 V at both input terminals of the op amp. It follows that IS = (VSRC – 10)/1 mA

Version 1: VSRC = 2 V, IS = VSRC – 10 = -8 mA

Version 2: VSRC = 4 V, IS = VSRC – 10 = -6 mA

Version 3: VSRC = 6 V, IS = VSRC – 10 = -4 mA

Version 4: VSRC = 8 V, IS = VSRC – 10 = -2 mA

Version 5: VSRC = 10 V, IS = VSRC – 10 = 0.

4%

3.	Determine VO, assuming VSRC = 1 V, and an ideal

op amp.

- -0.5 V

- 0.25 V

- 0.5 V

- -0.25 V

- 1 V

Solution: The second op amp

is an inverting amplifier of gain 2, so that VO2 = -2VO. Because of the

inversion in the feedback connection to the input of the first op amp, the feedback connection is to the noninverting input so as to have a negative feedback connection. This input is therefore a virtual ground. The current though the source is VSRC/20 mA and flows

through the 10 k( resistor, producing a voltage drop of VSRC/2 across this resistor. This voltage drop equals

-VO2, so that VSRC/2 = 2VO, or VO = VSRC/4.

Version 1: VSRC = 2 V, VO  = VSRC/4 = 0.5 V

Version 2: VSRC = 4 V, VO  = VSRC/4 = 1 V

Version 3: VSRC = 6 V, VO  = VSRC/4 = 1.5 V

Version 4: VSRC = 8 V, VO  = VSRC/4 = 2 V

Version 5: VSRC = 10 V, VO  = VSRC/4 = 2.5 V.

4%

4.	Determine the maximum magnitude of the lowpass response IO(j(), assuming the magnitude of ISRC(j() is 5 mA, all resistances are 4 k(, and all capacitances are 100 nF.

- 1 mA

- 0.5 mA

- 2 mA

- 1.5 mA

- 2.5 mA

Solution: The response is lowpass, since the capacitors behave as open circuits at low frequencies, and as short circuits at high frequencies. The resistors on the RHS have a resistance of 4 + 4/2 = 6 k(. It follows from current division that = 0.2.

Version 1: ISRC(j() = 5 mA, IO(j() = 0.2 ISRC(j() = 1 mA

Version 2: ISRC(j() = 10 mA, IO(j() = 0.2 ISRC(j() = 2 mA

Version 3: ISRC(j() = 15 mA, IO(j() = 0.2 ISRC(j() = 3 mA

Version 4: ISRC(j() = 20 mA, IO(j() = 0.2 ISRC(j() = 4 mA

Version 5: ISRC(j() = 25 mA, IO(j() = 0.2 ISRC(j() = 5 mA.

4%

5.	Determine the type of response VO(j()/VSRC(j() and its maximum value in dB (Note that the values of the circuit parameters need not be specified).

- Highpass, -3 dB

- Lowpass, -6 dB

- Lowpass, -3 dB

- Bandpass, 0 dB

- Highpass, -6 dB

Solution: As ( ( 0, the capacitor behaves as an open circuit and the inductor as a short circuit; VO(j() = 0. As ( ( (, the capacitor behaves as a short circuit and the inductor as an open circuit; ;  dB. Response is highpass.

4%

6.	The transfer function of a filter is of the form , where s = j( and A and B depend on circuit parameters but not on (. Determine B if the half-power frequencies are 20 krad/s and 45 krad/s.

- 30 (krad/s)2

- 25 (krad/s)2

- 900 (krad/s)2

- 200 (krad/s)2

- 450 (krad/s)2

Solution: B = rad2/s2.

20%

7.	Determine VO, assuming an ideal op amp.

Solution: The 2 k( and 1 k( resistors are in parallel. From current division, the current in the 1 k( resistor is 2 mA and that in the 1 k( resistor is 1 mA. Hence, VP = 2 V = VN. The current in the 4 k( resistor is therefore 0.5 mA flowing downward. From KCL, the current in the 6 k( resistor is 3.5 mA, and the voltage drop across this resistor is 6(3.5 = 21 V. It follows that VO = 21 + 2 = 23 V.

20%

8.	(a)	Derive H(j() = VO(j()/VSRC(j() and specify the type of response (10 grades).

(b)	Determine the maximum value of H(j() and the frequency at which it occurs (4 grades).

(c)	Determine the 3-dB bandwidth (2 grades).

(d)	Derive the expressions for the low-frequency and high-frequency asymptotes and specify their slopes in dB/decade (4 grades).

Solution: (a) It is convenient to work in terms of s and the half-power frequencies (C = 1/CR1 = 1/(5(10-6)(10-3) = 1000/5 = 200 rad/s, and (L = R2/L = 10/10-1 = 100 rad/s. From voltage division, , and . Subtracting the second expression from the first,  in standard form. The response is bandpass.

(b) From the standard form, the maximum value of H(j() = 1/3 and occurs at = rad/s.

(c) The 3-dB bandwidth is the coefficient of s in the denominator, which is 300 rad/s.

(d) As ( ( 0, H(s) ( 100s/(2(104), H(j() ( 100j(/(2(104) = j(/200, and |H(j()| ( (/200, which is a line of slope +20db/decade. As ( ( (, H(s) ( 100s/s2, H(j() ( 100/j(, and |H(j()| ( 100/(, which is a line of slope -20db/decade. The two lines intersect where , which gives rad/s. At this value of ( = (0, the magnitude of either asymptote 1/(3Q) = 1/, where Q = (0/BW = .

20%

9.	(a)	Derive H(j() = VO(j()/VSRC(j() and specify the type of response (12 grades).

(b)	Determine (0 and the maximum value of |H(j()| (2 grades each).

(c)	Determine Q and the 3-dB bandwidth (2 grades each).

Solution: Derive TEC as seen by the LC branch. ; RTh = 300||600 = 200 (. The circuit in terms of s becomes as shown. It follows that  . Multiplying numerator and denominator by s/L, substituting , and moving the 2/3 to the RHS, . The response is bandstop.

(b) rad/s ( 1.592 kHz; maximum response is = 0.667.

(c) BW is the coefficient of s, which is 200 rad/s ( 31.83 Hz; Q = (0/BW = 104/200 = 50. This is the same as (0L/R, or 1/(0CR, since the circuit is a series RLC circuit.