EECE 290 Analog Signal Processing, Sections 1, 2, and 3

Quiz 1 – March 17, 2007

Closed Book – One and One-Half Hours – 5:1 Penalty on Questions 1 to 6

(8%)

- Given f(t) as shown. Determine the convolution integral f(t)(2u(t) at t = 5 s.

  - 6

  - 8

  - 10

  - 12

  - None of the above

Solution: The convolution integral at t = 5 s is two times the area subtended by f(t):

2(3 + 3) = 12.

(8%)

2.	Determine the Laplace transforms of .

- 2

- 2

- 2

- None of the above

Solution: L {} = . Alternatively, ; L; multiplying by  changes the transform to ; multiplying by  gives the same result.

(8%)

3.	Given F(s) = L {f(t)}. If , determine lim f(t) as t ( (.

- 1

- -2/3

- 0

- infinity

- None of the above

Solution: . The inverse Laplace transform of the first fraction is , which tends to infinity as t ( (.

(8%)

4.	The impulse response of a given circuit is . What input to the circuit will produce an output that is ( (t), the unit impulse at the origin?

- None of the above

Solution: In terms of the Laplace transforms: F(s)(H(s) = 1, where . It follows that F(s) = s + 2, so that .

(8%)

5.	 An unknown voltage vSRC is applied to the circuit shown at t = 0, with zero initial conditions. If , what is iL(t)?

- tu(t)

- 2tu(t)

- None of the above

Solution: VO(s) =  = IO(s); VL(s) = ; IL(s) ; iL(t) = 2tu(t).

(8%)

6.	The switch has been in position a for a long time and is moved to position b at t = 0. Determine the Laplace transform of the current iS through the switch.

- None of the above

Solution: At , the two capacitors are charged to 10 V. The circuit in the s domain for t > 0 is as shown.

(17%)

7.	Determine the Laplace transform of the function f(t) shown.

Solution: The derivative of the function is as shown and can be expressed as:  . The Laplace transform of the derivative is: . Hence F(s) = .

Alternatively, F(s) =     = , as before.

(18%)

8.	Given that vI(t) is a pulse of 2 V amplitude and 1 s duration. Determine vO(t) in the circuit shown.

Solution: The impedance in the s domain of 1 H in series with 1 ( and in parallel with 1 F is . It follows that  . vi(t) = 2u(t) – 2u(t –1), so that Vi(s). = . The ILT is . It follows that vO(t) = V.

(17%)

9.	Given the functions f(t) and g(t) shown. Obtain the convolution integral for all t.

Solution: y(t) = f(t)(g(t) = 0, t ( 0.

At t = 1, y(t) = -1 and decreases linearly from 0 to -1 over the range 0 ( t ( 1. At t = 2, y(t) = 0 and increases linearly from -1 to zero over the range 1 ( t ( 2. At t = 3, y(t) = 1 and increases linearly from zero to 1 over the range 2 ( t ( 3. At t = 4, y(t) is again zero. y(t) will therefore be as shown.

As staircase functions, y(t) = 0 at t = 0 and t = 4. As polynomials, f(t) = t + 1, and g(t) = -t + 1. The product is . The breakpoints are (1, -1), (2, 0), and (3, 1), as determined previously.