Quiz 2 – Sections 1, 2 and 3

Open Book – One and One-Half Hours

8%

1.	A series RLC circuit is critically damped, i.e., . What is the Q of the circuit?

- 0.5

- 1

- 2

- 0

- None of the above

Solution: .

8%

- Determine the transfer

function whose Bode

magnitude plot is shown.

- None of the above

Solution: The low frequency asymptote is Ks. A pole must exist at 10 rad/s to reduce the slope to zero and another pole at 200 rad/s to give a slope of -20dB/decade. It follows that . To determine K, we note that at very low frequencies,  and , which must be the low-frequency asymptote. But this asymptote passes through the point (1 rad/s, 20dB). Hence, when s = j( = j, . Substituting, gives .

8%

3.	If a 4 M( resistor is connected in parallel with L and C, the bandwidth:

A.	increases by 20%

B.	decreases by 20%

C.	increases by 25%

D.	decreases by 25%

E.	None of the above,

Solution: Before the 4 M( resistor is added, Q = (0CR = (0C(1, and BW = . After the 4 M( resistor is added, R( = 4||1 = 0.8 M(. Hence, Q( = (0C(0.8, and BW( =  BW.

8%

4.	Given a bandpass transfer function of a series RLC circuit as , normalized to have (0 = 1 rad/s, C = 1 F, L = 1 H and R = 0.1 (. If the frequency is scaled so that (0 = 100 krad/s, and C = 100 nF, what would be the scaled value of Q?

A.	1

B.	0.1

C.	100

D.	10

E. None of the above.

Solution: In any type of bandpass filter, Q = . Both (0 and BW are scaled by the same factor, so that Q remains the same. For a series circuit, the coefficient of s in the denominator is . Hence, in the given transfer function, Q = 10 and remains 10 after scaling. This can be checked, for kf = 105 and , or , or km = 100, which gives R = 10 ( and 1 mH. It It follows that  rad/s and .

8%

5.	The circuit shown implements a filter of one of the following types:

A.	Lowpass

B.	Highpass

C.	Bandpass

D.	Bandstop

E. None of the above.

Solution: Qualitatively, the capacitors behave as open circuits at zero frequency. The input is isolated, and the output is connected to virtual ground, resulting in zero output. As ( ( (, the capacitors behave as short circuits, again connecting the output to virtual ground and resulting in zero output. Maximum output occurs at an intermediate frequency, resulting in a bandpass response.

Quantitatively, , which is a bandpass type response.

8%

- The circuit shown implements a first-order lowpass filter of variable cutoff frequency and a simulated large value of capacitance. The resistance between points a and b is (Rp, where 0 ( ( ( 1. The 3-dB cutoff frequency is:

A.

B.

C.

D.

E.	None of the above.

Solution: Because of the unity gain amplifier, the voltage of node a with respect to ground is Vo. The second op amp is an amplifier in the inverting configuration having Rr = (Rp and Rf = (1 – ()Rp. It follows that . The current . The effective capacitance at the noninverting input of the first op amp is C/(. The 3-dB cutoff frequency is therefore .

17%

- The op amp in the figure is ideal and of gain K.

(6%)	i)	Determine the frequency of maximum response.

(5%)	ii)	Find K so that the maximum response is 20 dB.

(6%)	iii)	Calculate the bandwidth.

Solution: , where C1 = 1F, R1 = 1 (, C2 = 0.5 F, and R2 = 0.5 (. This gives: .

- Substituting s = j(, . Maximum response occurs when ( = 2 rad/s.

- The maximum response is . To have this equal to 10, that is 20 dB, K = 50.

- At the half-power frequencies: . It follows that: ; ; 32.508 and 0.49219; (c = 5.702 and 0.702. The bandwidth is 5 rad/s.

Alternatively, by equating the coefficient of s in the denominator, which is 5, to the coefficient of s in the standard form of the second-order response, which is , it follows that . The bandwidth is rad/s.

17%

8. 	For the filter shown,

(6%)	i)	Determine the resonant frequency.

(6%)	ii)	If Vi = 1 V, determine the output at resonance and sketch the frequency response.

(5%)	iii)	Find Q.

Solution:

i)	rad/s.

ii)	At resonance, V. The sketch of the response is as shown.

iii)

.

18%

- Design a broadband bandpass filter consisting of a first-order lowpass active filter and a first-order highpass active filter to meet the following specification:

  - 3-dB cutoff frequencies of 10 Hz and 20 kHz.

  - A 1 nF capacitor is to be used in the lowpass filter and a 100 nF capacitor is to be used in the highpass filter.

  - Minimum input impedance of 10 k( resistive.

  - Overall gain of -10.

Assume ideal op amps. Draw the circuit diagram showing all component values.

Solution: Since the 3-dB cutoff frequencies are more than a decade apart, each filter can be designed separately. To have a cutoff frequency of 20 kHz for the lowpass filter requires Rfl = k(. For the highpass filter, Rrh =

k(. If Rrl = 10 k(, the gain of the two filters is = . If Rfh = 200 k(, the overall gain is 1. To have a gain of 10, an inverting amplifier of gain -10 should be added. This can have Rr = 1 k( and Rf = 10 k(. The complete circuit is as shown.