Test 4

(March 12, 2007)

The switch is closed at t = 0, with vSRC(t) = 6cost V and no initial energy storage in the circuit. Determine:

40%	i)	Vo(s)

40%	ii)	vO(t)

20%	iii)	What are vO(0+) and vO(t) as t ( (, and Why?

10% Bonus: Compare with vO(t) using phasor analysis

Solution: i) The 1 F capacitor, being in parallel with an ideal voltage source is redundant as far as the output is concerned. The parallel impedance of the 3 H inductor and 0.5 F capacitor is . It follows that ; ; .

ii) From the multiplication-by-t property: L. Hence, .

iii) , because no current flows at t = 0 through the 6 H inductor. The response is unbounded as t ( (, because the frequency of excitation is the same as that of the pole.

From phasor analysis: VSRC = 6(0(, ( = 1. Substituting s = j(= 1 in the transfer function , VO = , which gives vO(t) ( (. Phasor analysis does not apply in this case, because it is valid only for the sinusoidal steady state. But the circuit never reaches a steady state.