Main concepts in Electrostatics

Maxwell’s equation for electrostatics:

Where

D: Electric field density (N/m)

E: Electric field intensity (N/m)

Force acting on a point charge exposed to an electric field:

F=qE  (N)

Charge calculation:

The total charge contained in a given volume  is given by

For a surface charge distribution:

For a line charge distribution:

Coulomb’s law to get the electric field due to a charge distribution:

Volume charge distribution:

Surface charge distribution:

Line charge distribution:

Examples:

- Discrete charges:

- Infinitely long line:

- Infinite sheet: 	 (for a point above the sheet and the opposite for a point below it)

For the following cases, all charge distributions are on the xy plane and we are considering E at P(0,0,h)

- Circular ring:

- Ring with inner radius a and outer radius b:

- Disk of radius a :

Gauss’s law to get the electric field due to a charge distribution:

Electric scalar potential:

By taking P1 at infinity,

Electric field as a function of electric potential

Electric potential in Boundary value problem:

Electric polarization vector:

P=ε0 χ E

So D= ε0E+P= ε0(1+ χ)E where εr= χ +1

Calculation of the resistance:

Procedure that can be useful for calculating the resistance of a conductor in many cases:

- Choose an appropriate coordinate system for the geometry.

- Assume a potential difference Vo between the conductor terminals.

- Find E within the conductor.

- Find the total current as

- Find the resistance as  in Ω

Conductance: G=1/R in Siemens (S)

Calculation of the capacitance:

Procedure for calculating the capacitance in many cases:

- Choose an appropriate coordinate system.

- Assume +Q and –Q on the conductor.

- Find E from Q using Gauss law or other relations.

- Find V: V=

- C=

Examples:

  - Parallel plate capacitor: C= εS/d

  - Cylindrical capacitor: C= 2πεL/ln(b/a)

Electrostatic energy:

And Q=CV

For discrete charges,

Electrostatic Force:

Material characteristic:

Electric Boundary conditions:

Consider,

(

For a perfect conductor,

Parameters: