Previous Exam Questions – Diodes

EECE310 Electronics I – Section 1 (N. Sabah)

Quiz 1 – November 12, 2005

One Hour and a Half – Closed Book

3:1 Penalty – Programmable Calculators Not allowed Unless Reset

Each of the 20 answers in Questions 1 to 6 is assigned two grade points. Each of the three problems is assigned 20 grade points.

1.	A thin slab of intrinsic semiconductor has been illuminated for a long time with light of appropriate wavelength so that the total rate of generation of electron-hole pairs is 1022/s/cm3, the concentration of electrons is 1015/cm3, but no current flows.

(a) Is the semiconductor at equilibrium?

(b) What is the concentration of holes?

(c) What is the rate of recombination?

(d) If the concentration of carriers is multiplied by a factor of 103, by what factor is the conductivity multiplied?

(e) What is the mean carrier lifetime?

Answers: (a) No, because the semiconductor is disturbed by the radiation. It is in a steady state.

(b) The same as that of electrons, because the semiconductor is intrinsic and electrons and holes are generated in pairs and recombine in pairs.

(c) Same as the rate of generation, in the steady state.

(d) Conductivity is proportional to carrier concentration and increases by the same factor.

(e) If the recombination rate is 1022/s/cm3, and the concentration is 1015/cm3, then the rate of recombination per carrier is 107/s, so the carrier lifetime is 10-7 s.

- A slab of p-type semiconductor is non-uniformly doped, so that NA varies along the slab as shown. Under equilibrium conditions, will sides A and B be at the same voltage. If not, which side will be at a more positive voltage?

Answer: Since the system is at equilibrium, the electrochemical potential of holes is the same throughout the slab. With holes more concentrated on side A with respect to side B, they are at a higher chemical potential, so they must be at a lower electric potential, which means that side B is at a more positive voltage.

3.	A junction is formed between an n-type semiconductor and an intrinsic semiconductor. Under equilibrium conditions:

(a) On which side are holes more concentrated?

(b) Which side will be at a more positive voltage?

Answers: (a) On the intrinsic side, because hole concentration in the n-type semiconductors suppressed below ni.

(b) The n-side, because holes diffuse from the intrinsic to the n-side, and electrons diffuse in the opposite direction.

4.	In a pn junction, the p-side is much more heavily doped than the n-side. The doping level on the p-side is increased even further.

(a) What happens to the depletion capacitance at equilibrium?

(b) What happens to the breakdown voltage, assuming avalanche breakdown?

(c) Which current, electron or hole, predominates under forward bias?

(d) Which current, electron or hole, predominates under reverse bias?

Answers: (a) The depletion region is much wider on the n-side than on the p-side. It becomes narrower on the p-side. This is similar to forward bias, which increases the depletion capacitance.

(b) The breakdown voltage is not affected significantly because it is determined by the doping level on the n-side.

(c) The current under forward bias is a majority-carrier current. Since the concentration of holes on the p-side exceeds the concentration of electrons on the n-side, the hole current predominates.

(d) The current under reverse bias is a minority-carrier current. Since the concentration of holes on the n-side exceeds the concentration of electrons on the p-side, the hole current predominates.

5.	When the temperature of a pn junction diode is raised,

(a) Which current increases faster, iD or IS?

(b) What happens to Vd0?

(c) What happens to the current of a photodiode?

(d) What happens to the wavelength of light emitted by an LED.

Answers: (a) IS, because the change in the exponential term opposes this change.

(b) Decreases, because the v-i curve is shifted to the left.

(c) Increases, because ISS increases with the rate of generation of carriers.

(d) Eg and hence ( decrease, so that ( increases.

6.	Choose the appropriate phrase (allow free motion of electrons, allow free motion of holes, allow generation of electron-hole pairs, allow recombination of electrons and holes) to complete each of the following statements:

(a) The metallic contact on the n-side should …… under forward bias and should …… under reverse bias.

(b) The metallic contact on the p-side should …… under forward bias and should …… under reverse bias.

Answers: (a) Allow free motion of electrons in both cases.

(b) allow generation of electron-hole pairs, allow recombination of electrons and holes

7.	 Determine the diode currents in the circuit shown, assuming ideal diode switches.

Solution: To have some guidance concerning circuit behavior, assume that the circuit is separated into two, as shown. Then Va = -10 + (6 k()(5 mA) = 20 V. The current in the two diodes is 1 mA, so that Vb = -6 + (7 k()(1 mA) = 1 V. This suggests that when a and b are joined together, the voltage of b is pulled up, which turns off D1. Assuming D1 is off, and that the current in D2 is I2 mA, KVL gives: -6 + 7I2 = -10 + 6(5 – I2). Hence, I2 = 2 mA. The voltage at the junction of the two diodes is -6 + 14 = 8 V. this confirms that D1 is off. It follows that I1 = 0, and I2 = 2 mA.

- The triangular wave shown is applied to a CTT rectifier supplying a constant current load of 100 mA through a capacitor-input filter, the peak half-secondary voltage being 10 V. The conduction interval during the first period is found to be from t = 1.98 ms to t = 2 ms. Assuming ideal diode switches, determine: (a) the peak-to-peak ripple, (b) the size of the filter capacitor, and (c) the size and shape of the diode current. No approximations should be made.

Solution: (a) The magnitude of the slope is 20 V/ms. The voltage change in 0.02 ms is 0.4 V, which is the peak-to peak ripple vr. (b) During nonconduction, (Q = Cvr, where (Q = 100(0.98 = 98 (C. Substituting. (F. (c) During conduction, = (245 (F)((20(10-3 V/(s) + 0.1 = 5 A. the diode current is therefore a rectangular pulse of 5 A. Note that the average diode current is then 50 mA, since diodes conduct on alternate cycles.

- The periodic waveform whose first period is illustrated is applied to the circuit shown. The diodes are identical and may be considered to have a forward voltage of 1 V and a breakdown voltage of 5 V for all forward or reverse currents, respectively. The capacitor is so large that its voltage may be considered to remain nearly constant in the steady state. Determine the steady-state values of: (a) the average voltage VC across the capacitor; (b) the average output voltage VO.

Solution: (a) Let us assume that the two diodes conduct in both the forward and reverse directions and check the validity of this assumption. When vI = 10 V, the circuit is as shown.  () mA. The charge gained by the capacitor is ()(1 mC.

When  V, the circuit is as shown.

. The charge lost by the capacitor is  mC. In the steady state, the charge gained equals the charge lost. Hence, , or V.

With this VC the diodes will conduct in the reverse direction.

(b) In terms of average, or DC, values, .

V. Hence,  V.

Final Exam – June 2006

5.	In the circuit shown, vSRC is a periodic rectangular wave that has a value of 10 V for 2 ms and – 5 V for 1 ms. Determine VC, the average value of capacitor voltage in the steady state, assuming ideal diodes and R = 2 k(.

A.	8 V

B.	7.5 V

C.	7 V

D.	6.25 V

E.	None of the above.

Solution: In the steady state, the charge gained by C during the positive phase is equal to the charge lost during the negative phase. Hence, ; V.

9.	Assume V1 = 20 V, V2 = 4 V, R1 = 4 KΩ, R2 = 8 KΩ. Using the constant voltage drop model for the diodes (0.7V), find the current that passes through D2.

- 1.825 mA	B.	1.175 mA

C.	0.65 mA	D.	3 mA

E.	None of the above

Solution: Since V1 >> V2, it would be expected that both diodes are ON. The voltage across R1 is 4.7 V and the current through R1 is 4.7/4 = 1.175 mA. From KVL: 20 – 0.7 = 4.7 + 8(ID2 + 1.175); ID2 = 0.65 mA.

13. 	For the zener regulator shown, VS = 9 ( 1 V, Rs= 100 (, Vz= 7 V at Iz= 20 mA and rz= 15 (. Determine IL when RL= 1.2 k and VS is maximum.

A.	5.79 mA	B.	5.88 mA	C.	5.77 mA

D.	5.96 mA	E.	None of the above

Solution: , Vz0 = 6.7 V; from KVL: Vsmax = Rs(IZ + IL) + RLIL = RsIZ + (Rs + RL)IL. But RLIL = Vz0 + 0.015IZ, or ; Vsmax + =

. Substituting: 10 + , IL = 5.88 mA.

14.	In the zener regulator of the preceding problem, determine the minimum load resistance that can be connected at the output while the regulator still operates properly with the zener diode current above its knee value Izk= 0.5 mA.

A.	430 (	B.	240 (	C.	624 (

D.	540.0 (	E.	None of the above

Solution: Vsmin = Rs(IZ + IL) + RLIL = RsIZ + (Rs + RL)IL. But RLIL = Vz0 + 0.015IZ, or ; Vsmin – Vz0 – (Rs + 0.015)IZ = . Substituting: , or RL = 540.0 (

20.	The characteristics of both diodes are such that at equal diode voltages ID1 = 2ID2. Assume n = 1 and VT = 25 mV. The battery voltage is 1.5 V. What is the value of V2?

A.	0.759 V

B.	0.835 V

C.	0.910 V

D.	0.607 V

E.	None of the above

Solution: ; ; hence, ; ; ;  V.