EECE 310 Electronics – Section 1

Quiz 1 – November 3, 2007

CLOSED BOOK – One and One-Half Hours

Penalty 5:1 on Questions 1 - 7

(7%)

- In the given circuit, VSRC = 5 V dc and the diode is an ideal diode switch. Determine the dc current I so that the reverse voltage across the diode is 2 V.

A.	5 mA

B.	-5 mA

C.	-7 mA

D.	6 mA

E.	None of the above

Solution: When the ideal diode switch is reverse biased, it behaves as an open circuit. From KVL: -VR = VSRC + I(1 = 0;

-2 = 5 + I, or I = -7 mA.

(7%)

- In the given circuit, vSRC =  V. The diode may be modeled as having VD0 = 0.6 V and rD = 5 (. Determine t at which the diode will just begin to conduct in the forward direction.

A.	1.25 ms

B.	1.67 ms

C.	1.84 ms

D.	2.12 ms

E.	None of the above

Solution: At the instant of conduction, the forward voltage across the diode is 0.6 V and the current through the diode is zero. It follows that vSRC = = 5(0.6 = 3 V. This gives ; ms.

(7%)

- In the given circuit, the zener diode may be modeled as having VZ0 = 5 V, rZ = 0, and in the forward direction as having VD0 = 1 V, rD = 0. vSRC is the periodic waveform shown. Determine the average value of vL.

A.	5 V

B.	1 V

C.	3 V

D.	2 V

E.	None of the above

Solution: During the positive half-cycle, the diode behaves as a zener diode, and vL = VZ0 = 5 V. During the negative half-cycle, the diode conducts in the forward direction, and vL = 1 V. The average value is  V.

(7%)

- Determine the average value of vR in the preceding problem.

A.	0.5 V

B.	-0.5 V

C.	1 V

D.	3 V

E.	None of the above

Solution: During the positive half-cycle, vR = 10 – 5 = 5 V. During the negative half-cycle, vL = -4 V. The average value is  V. Alternatively, it can be argued that: average vSRC = average vR + average vL. Since average vSRC = 2.5, it follows that average vR = 2.5 – 2 = 0.5 V.

(7%)

- In the circuit shown, the diodes can be modeled in the forward direction by VD0 = 0.7 V, rD = 0. At what value of vI (not vO) will limiting just begin?

A.	0.7 V

B.	1.2 V

C.	1.4 V

D.	2.4 V

E.	None of the above

Solution: When limiting just begins, the upper diode will present a voltage of 0.7 V. Current can flow in the 1 k( resistor, which at the beginning of limiting will be very small, so that the lower diode does not conduct. Hence, limiting will just begin when vO = 0.7 V. At this value of vO the current in the 1.4 k( resistor is 0.5 mA, which causes a voltage drop of 0.5 V across the series 1 k( resistor. It follows that vI = 0.5 + 0.7 = 1.2 V.

(7%)

- A p-type semiconductor having a majority carrier concentration of 1017/cm3 is in contact with an intrinsic semiconductor in the same crystal. Determine the electric potential of the intrinsic semiconductor with respect to the p-type semiconductor, assuming ni = 1010/cm3 and VT = 0.026 V.

A.	0.23 V

B.	0.38 V

C.	0.42 V

D.	0.57 V

E.	None of the above

Solution: At equilibrium, the electrochemical of holes must be the same in both types of semiconductor, where . In the p-type semiconductor, , whereas in the intrinsic semiconductor, . Equating (hp to (hi, Cr, Vr, and (r cancel out, giving V.

(7%)

- An n-type semiconductor has ND = 1018/cm3. At the temperature under consideration, the donor impurities are 90% ionized, ni being 108/cm3. Determine the equilibrium concentration of majority carriers.

A.	108/cm3

B.	9(108/cm3

C.	9(1017/cm3

D.	1018/cm3

E.	None of the above

Solution:  = 0.9(1018.

(17%)

- An x-ray machine requires a dc voltage of 150 kV at a dc current of 100 mA, with peak-to-peak ripple of 500 V. A half-wave (not full-wave) rectifier with a capacitor-input filter is to be used. (a) If at this voltage, a 0.01 (F capacitor is practicable, what should be the supply frequency? (b) If the transformer used has a primary voltage of 100 V rms, what should be the primary-to-secondary turns ratio.

Solution: (a) Assuming that the approximate analysis holds, then for the half-wave rectifier, , or kHz. To check the validity of the approximate analysis,  600.

(b) . Since vr << VDC,  kV. The diode voltage drop is also small compare to , so that  = 150 kV. The rms secondary voltage is . The primary-to-secondary turns ratio is , or , or .

(17%)

- Given a zener diode regulator using a zener diode of VZ0 = 9 V and IZmin = 2 mA. The input varies between VImax and VImin, where VImax – VImin = 5 V. A variation of the load current between zero and 20 mA, at constant input voltage, changes the load voltage by 0.2 V. A change in the input voltage between VImax and VImin changes the load voltage by 0.1 V, at a constant load current of 20 mA. Determine: (a) RS; (b) rZ; (c) VZ at IZ = 10 mA; (d) VImin; and (e) minimum power rating of zener diode.

Solution: At constant input voltage, , or, . At constant load current: . Dividing gives:

(a) (.

(b) It follows that , so that  (.

(c) 9.10 V;

(d) At IZ = 2 mA,  V;  V;

(e) , which gives mA,  9.32 V; minimum power rating of zener diode = 9.32(0.0314 = 0.293 W.

(17%)

The waveform of Problem 3 is applied to the circuit shown. Determine VC assuming a very large capacitor

Solution: C is discharged during the positive half cycle, the discharge current being mA. The charge lost is . During the negative half cycle, C is charged, the charging current being mA. The charge gained is . Equating these: , so that VC = 10.5 V.