EECE 310 Electronics I – Section 1 (N. Sabah)

Quiz 2 – December 8, 2007

One Hour and a Half – Closed Book

5:1 Penalty on Questions 1 to 7

ALL QUESTIONS MUST BE ANSWERED ON THE QUESTION SHEET

NAME:	___________________________________________________

ID:	___________________________________________________

7%

1.	Given two pn junctions i) pn junction 1 having ND1 = 1016/cm3 and NA1 = 1014/cm3, and ii) pn junction 2 having ND2 = 1014/cm3 and NA2 = 1016/cm3. Which pn junction will have the larger magnitude of junction potential?

- pn junction 1

- pn junction 2

- Both pn junctions will have the same magnitude of junction potential

- None of the above

Solution: The magnitude of the chemical potential difference is . Since this is the same in both cases, the magnitude of the electrical potential difference will be the same.

7%

2.	NA and ND on the two sides of a pn junction are varied but their product is kept constant at 1032/cm6. For what NA and ND is the width of the depletion region W, a minimum?

- NA = ND

- NA > ND

- NA < ND

- NA = ND but W is a maximum

- None of the above

Solution: , where everything is constant except (NA + ND). The sum is a minimum when NA = ND. Thus, if y = NA + , where K = NAND, , which gives NA = ND. That this is a minimum is clear from .

7%

3.	If the temperature increases, the open circuit voltage of a photocell:

- increases

- decreases

- stays the same

Solution:  – ISS, where, ISS = AJGx(Wd + Lh + Le). Wen iD = 0, Voc = . ISS changes weakly with T but IS increases exponentially with T. Hence, VOC decreases with T.

7%

4.	A normal pn junction diode having ( = 1 is paralleled with a Schottky diode of the same junction area. Which diode will carry the larger current?

- The normal pn junction diode.

- The Schottky diode.

Solution: The Schottky diode equation is , and the equation for a normal diode having ( = 1 is . IB0 >> IS, so that for the same vB, the Schottky diode will carry the larger current.

7%

5.	In the circuit shown, VDD = 5 V, Vt = 1 V, C is initially discharged, and vI suddenly increases from zero to a steady value VDD. The final value of vC is:

- 5 V

- 4 V

- 3 V

- 1 V

- None of the above

Solution: When vI increases from zero to VDD, with vC = 0 initially, vGS = VDD, iD flows, C charges, vC increases, and vGS and iD decrease. iD becomes zero when vGS = Vt. The final value of vC is therefore, VDD – Vt = 5 – 1 = 4V.

7%

6.	The E-NMOS transistor has  (A / V2, , Vtn = 1 V and ( = 0. If it is replaced by a D-NMOS transistor whose transfer characteristic is that of the E-NMOS transistor shifted by 3 V, the D-NMOS transistor will be:

- in the triode region

- in the saturation region

- cut-off

- None of the above

Solution: VGS = 2 V, VtnD = 1 – 3 = -2 V; assuming transistor is in saturation,  mA. This makes vDS < 0, which means the assumption is wrong and the transistor is in the triode region. To confirm this, iD and vDS can be found by solving the equations:  and vDS + iD = 5. This gives  mA, vDS = 1.13 V; vDS < vGS – VtnD, which confirms that transistor is in triode region.

7%

7.	The E-NMOS transistor of the preceding problem is replaced by a matched E-PMOS transistor with its drain grounded and its source connected to the 1 k( resistor. The EPMOS transistor will be:

- in the triode region

- in the saturation region

- cut-off

- None of the above

Solution: VSG = 3 – iD; VSD = 5 – iD. Assuming that the transistor is in the saturation region,  . This gives iD = = 0.764 mA and 5.24 mA. The latter is discarded because it makes vSG and vSD negative. Hence, iD = 0.764 mA; vSG = 2.24 V and vSD = 4.24 V, which confirms that the transistor is in saturation.

17%

8.	In the circuit shown, VSS = -5 V and R = 2 k(. The transistor has  (A / V2, , Vtn = 1 V and ( = 0.

12%	(a)	Determine the transistor current.

5%	(b)	If  and the transistor has the same operating conditions, determine the incremental output resistance of the transistor as seen by R.

Solution: (a) VGS + 2ID – 5 = 0, or VGS = 5 – 2ID. The transistor is in saturation, because its drain and gate are at the same voltage. . Substituting for VGS,  , or , which gives ID = 1 mA or 4 mA. If ID = 4 mA, VGS = -3 V, which is impossible. Hence, ID = 1 mA and VGS = 3 V.

(b)  mA / V. this makes ro = 100 k(. gm = 0.5(2(1.03 = 1.03 mS, Output resistance is rO||(1/gm) = 0.97 k(.

17%

9.	In the circuit shown, Q1 and Q2 have  mA / V2, Vt = 0.8 V, , 0.05 V-1, (W/L)n1 = 10, and (W/L)n2 = 20. Determine IO.

Solution: Q1 is in saturation, so 1 = ; hence,  V. Assuming Q2 is in saturation, IO = = 2 + 0.1VDS2. From KVL, VDS2 + 0.5IO = 5, or VDS2 = 5 – 0.5IO. Substituting, IO = 2.38 mA and VDS2 = 3.81 V, which confirms that Q2 is in saturation.

17%

10.	The transistors of a CMOS inverter operating from a VDD = 3 V supply have the following parameters:

E-NMOS:	120 (A/V2,	(W/L)n = 4	Vtn = 0.6 V	( = 0

E-PMOS:	50 (A/V2,	(W/L)p = 6	Vtp = -0.7 V	( = 0

Determine the input voltage vI that makes the inverter operate on the vertical segment of its transfer characteristic.

Solution: Over the vertical segment of the transfer characteristic, both transistors operate in the saturation region, with equal currents. For Qn: iDn = . For Qp:  . Equating the currents:  , or . This gives   V, or -5.81 V. The negative value is discarded, so that vI = 1.35 V.

Useful Equations

– ISS, where, ISS = AJGx(Wd + Lh + Le)

For the Schottky diode:

(saturation region)

(triode region)