## Slide 1: EECE 311: Electronic Circuits Part 3

## Slide 2: Common Source Amplifier with Source Resistance
Small Signal Model at Low Freq:
What does RL model?
Note that vi ≠ vgs

## Slide 3: Common Source with Source Resistance
The current flows in RS
Voltage gain:
  Reduced by factor (1+ gm RS)
What is the input resistance?
What is the output resistance?

## Slide 4: Common Source with Source Resistance Do not neglect channel length modulation (ro)
Thevenin - Norton

## Slide 5: Common Source with Source Resistance Do not neglect ro
ro causes the gain to drop (further)
i

## Slide 6: Common Source with Source Resistance Do not neglect ro
What is the input resistance?
What is the output resistance?

## Slide 7: Common Source with Source Resistance Do not neglect ro
Output resistance?

## Slide 8: Common Source with Source Resistance Do not neglect ro
Output resistance
RXY = RX + RY + gm RX RY
Ro = ro + RS + gm ro RS
Looking into the drain of a MOSFET, with gate at DC (no signal), and resistance RS between source and ground, a resistance ro + RS + gmroRS is seen (from drain to ground).

## Slide 9: BJT Common-Emitter with RS Small-Signal Equivalent Circuit

## Slide 10: Input Resistance of CE with RS
Ri = vi / ii
vp = rp ii
vi = vp + Rs (ii + gm vp)
= rp ii + RS (ii + gm rp ii)
vi / ii = rp + RS (1 + gm rp)
But gm rp = b :
Ri = vi / ii = rp + (b + 1)RS

## Slide 11: BJT Base Reflection Rule
The resistance seen looking into the base is:
rp + (b + 1) times the resistance between the emitter and ground
…the resistance in the emitter appears (b + 1) times larger when looking into the base.
Fine print: The above rule applies when ro is very large (negligible Early Effect)

## Slide 12: BJT Common-Emitter Small-Signal Equivalent Circuit
Voltage gain:
Similar to MOSFET result

## Slide 13: BJT Common-Emitter with RS Output Resistance
Hint: Recycle!
Output resistance:
use MOSFET result
after noting that
rp and RS are connected in parallel for the Ro calculation (when vi is set to zero):
Ro = ro + (rp // RS) + gm ro (rp // RS)

## Slide 14: Common-Gate Amplifier with Active Load

## Slide 15: Common-Gate Amplifier
  Input Resistance:
  Voltage gain:
  Output resistance:
  Current gain:

## Slide 16: Resistance Looking into MOSFET Source Terminal
The resistance seen looking into the MOSFET source with gate at DC levels (no signal) is equal to 1/gm
Does NOT apply when ro is not neglected (not )
  1/gm becomes an approximation

## Slide 17: Common-Gate Amplifier (with ro)
  Input Resistance
Note
We calculated Rin and not Ri
Rin depends on RL

## Slide 18
  Open-Circuit Voltage Gain
  Voltage Gains (RL connected)
Note
Av , Gv are positive (non-inverting)

## Slide 19
  Output Resistance
    Rout = output resistance with vsig = 0
  Common Gate Characteristics
    Large Output Resistance
    Small Input Resistance
    Unity Current Gain
Good current buffer
    Ro = output resistance with vi = 0

## Slide 20: Common-Gate at High Frequency (no ro)
Note: body is grounded

## Slide 21
  Considering ro
Note
No Miller (multiplication) effect
Larger bandwidth than Common-Source

## Slide 22: Common-Base Amplifier
Small Signal Model:

## Slide 23
  Input Resistance
very small input resistance

## Slide 24
  Output Resistance

## Slide 25: Cascode Amplifier
Common-Source + Common-Gate

## Slide 26
  Input Resistance:
  Output Resistance:
    The last stage is a common-gate
the signal source resistance of the common-gate stage is the output resistance of the common-source stage.

## Slide 27
  Voltage Gain
  Open-Circuit Voltage Gain of Cascode
  Voltage Gain with Load Connected

## Slide 28
  Cascode High Frequency Response

## Slide 29
  Resistance seen by Cgs1

## Slide 30
  Resistance seen by Cdb1+Cgs2+Csb2

## Slide 31
  Resistance seen by CL+Cgd2+Cdb2

## Slide 32
  Resistance seen by Cgd1

## Slide 33
We use the results derived previously for input and output resistances of common-source and common-gate stages

## Slide 34: Cascode Current Source
Large Output Resistance
Serves well as a current source (load) for an amplifier

## Slide 35
BJT Cascode

## Slide 36
  Open-Circuit Voltage Gain
  Input Resistance by inspection
  Output Resistance
CB formula

## Slide 37: Common Drain (Source Follower)
Small Signal Model:

## Slide 38
Small-signal equivalent circuit:
  Input Resistance
  Voltage Gain
  Open-Circuit Voltage Gain

## Slide 39
  Output Resistance

## Slide 40: Common Drain with channel length modulation (ro)
Small Signal Model:

## Slide 41
Equivalent Circuit:
  Input Resistance
  Voltage Gain
  Open-Circuit Voltage Gain

## Slide 42
  Output Resistance

## Slide 43: Common Collector (Emitter Follower)

## Slide 44
  Input Resistance
  Voltage Gain
  Open Circuit Voltage Gain
Large Input Resistance
Open Circuit Voltage Gain nearly one: Signal at emitter “follows” signal at input

## Slide 45
  Output Resistance
Very Low Output Resistance

## Slide 46: Some Useful Transistor Pairings
Common Collector – Common Emitter Pairing
Wide Bandwidth
Large Input Resistance

## Slide 47
Darlington Pair
High-Performance Voltage Follower

## Slide 48
Common Drain – Common Gate Pairing
Infinite Input Resistance
Voltage gain ~ ½ CG
Very Good High Frequency Response

## Slide 49
Common Collector – Common Base Pairing
PNP Common-Base Stage
Very Good High-Frequency Performance

## Slide 50: Improved Current Sources
Larger output resistance (current less dependent on voltage – closer to ideal)
Less dependence on transistor parameters (such as  in BJT)
Without sacrificing voltage range?
  Voltage across real current sources (VCS) cannot drop below a certain minimum

## Slide 51
Cascode MOS Mirror
Large output resistance
But reduced range of VO

## Slide 52
Improved Bipolar Current Mirror
Dependency on β decreased from 1/ β to 1/ β2 (error term is β times smaller)
But output resistance still the same (ro2)
What about voltage range?

## Slide 53
Wilson Current Mirror
Dependency on β decreased from 1/ β to 1/ β2
Output resistance multiplied by β/2
But reduced range of Vo (Vomin = 1V)

## Slide 54
Wilson MOS Mirror
Large output resistance
But reduced range of VO

## Slide 55
Improved Balanced Wilson MOS Mirror
Same as Wilson MOS current but with balanced drain voltages of Q1 and Q2.

## Slide 56
Widlar Current Source
Can generate a small constant current using relatively small resistors.