a) Write a MIPS R2000 assembly subroutine that searches for the last occurrence

of a string s1 in another string s2. If s1 is found in s2, your subroutine must

return a pointer (i.e. the address) to the last location in s2 where s1 is

found; otherwise, your subroutine must return zero. Assume both s1 and s2 are

null terminated, that the starting addresses of s1 and s2 are passed as

parameters to the subroutine in registers $a0 and $a1, and that the result of

the subroutine is returned in register $v0. Include short comments in your

code.

Answer:

.text

add        $t0,$a0,$0                # Calculate length(s1) and store it in $t1

add        $t1,$0,$0

L1:                lb        $t2,0($t0)

beq        $t2,$0,L2

addi        $t1,$t1,1

addi       $t0, $t0, 1

j        L1

L2:                beq        $t1,$0,END0                # If $t1 == 0, return zero

add        $t0,$a1,$0                # Calculate length(s2) and store it in $t3

add        $t3,$0,$0

L3:                lb        $t2,0($t0)

beq        $t2,$0,L4

addi        $t3,$t3,1

addi       $t0, $t0, 1

j        L3

L4:                beq        $t3,$0,END0                # If $t3 == 0, return zero

slt        $t0,$t3,$t1                # If $t3 < $t1, return zero

bne        $t0,$0,END0

sub        $t0,$t3,$t1                # Initialize $v0 to &(s2[length(s2)-							 # length(s1)])

add        $v0,$a1,$t0

L5:                addi        $t0,$v0,$0          # Use $t0 and $t1 as s2 and s1 								 # pointers, respectively

addi        $t1,$a0,$0

L6:                lb        $t2,0($t0)                # Use $t2 and $t3 as s2 and s1 							   # characters, respectively

lb        $t3,0($t1)

beq      $t3, $0, END		# check if end of s1 has been reached

# If $t3 == 0 return; $v0 points

# to location of s1 in s2

bne        $t2,$t3,L7                # If $t2 != $t3 decrement

addi        $t0,$t0,1

addi        $t1,$t1,1

j        L6

L7:          addi        $v0,$v0,-1                # decrement $v0 and try 							             # to find a match again

slt        $t0,$v0,$a1                # If $v0 < $a1, return zero

bne        $t0,$0,END0		 # no match

j        L5

END0:                add        $v0,$0,$0

END:                jr        $ra

b) Write a MIPS R2000 assembly subroutine that replaces the last n characters of

a string s1 by the character c. Assume s1 is null terminated and that the

subroutine is passed three parameters -- the starting address of s1, an

unsigned integer n, and the ASCII code of the character c -- in registers $a0,

$a1, and $a2, respectively. You may also assume that n is less than or equal to

the length of the string. If the subroutine is successful, it must return the

value one (0x00000001) in register $v0; otherwise it must return zero

(0x00000000). Include short comments in your code.

Answer:

.text

add        $t0,$a0,$0             # Calculate length(s1) and store it in $t1

add        $t1,$0,$0

L1:                lb        $t2,0($t0)

beq        $t2,$0,L2

addi        $t1,$t1,1

addi        $t0,$t0,1

j        L1

L2:                beq        $t1,$0,END0                # If $t1 == 0, return zero

sub        $t0,$t1,$a1                # Initialize $t2 to &(s1[length(s1)-n])

add        $t2,$a0,$t0

L3:                sb        $a2,0($t2)                # Iterate over the characters pointed 					         # to by $t2 and replaced them with $a2

addi        $t2,$t2,1

addi        $a1,$a1,-1

bne        $a1,$0,L3

END:                addi        $v0,$0,1

jr        $ra

END0:                add        $v0,$0,$0

jr        $ra

Question 2: Subroutine Linkage


V1) The main portion of a MIPS assembly program contains a call to a subroutine
A. Subroutine A does not call any other subroutine and returns to the main
program once it completes execution.

a) If the main program has important data stored in register $s3, does it need
to save it on the stack before calling subroutine A? Explain.

Answer: No. The main program does not need to store register $s3 since it will
be preserved (i.e. saved and later restored) by subroutine A.

b) If subroutine A needs to use register $t6, does it need to save it on the
stack first? Explain.

Answer: No. Since register $t6 is not preserved across a subroutine call,
subroutine A does not need to save it.

c) Once it starts executing, does subroutine A need to save $sp, $fp, and $ra on
the stack? Explain.

Answer: No. Since subroutine A does not call another subroutine, it does not
need to save $sp, $fp, or $ra.

d) If the main program needs to pass three additional arguments to subroutine A
beyond those passed in registers $a0 to $a3, and if those arguments are stored
in registers $t2,$t3, and $t4, show the sequence of instructions that must be
executed immediately before the subroutine call. Include the subroutine call in
the sequence of instructions.

Answer:

addi        $sp,$sp,-12
sw        $t2,8($sp)
sw        $t3,4($sp)
sw        $t4,0($sp)
jal        subroutine_A

e) While executing subroutine A, the subroutine needs to access the argument
that was originally stored in register $t3. Assuming subroutine A saves
registers $s0 to $s3 on the stack, show the assembly instruction that can be
used to retrieve this argument. Explain using a stack diagram.

Answer: The following diagram shows the stack during the execution of subroutine
A:

$t2
$t3
$t4
----
$s0        <-- $fp
$s1
$s2
$s3        <-- $sp

The argument that was originally stored in register $t3 can be accessed by
executing the following instruction:         lw        $t3,8($fp) or lw        $t3,20($sp)

-----------------------------


V2) The main portion of a MIPS assembly program contains a call to a subroutine
A. At some point, subroutine A calls subroutine B and returns to the main
program once both subroutines have completed execution.

a) If the main program has important data stored in register $t3, does it need
to save it on the stack before calling subroutine A? Explain.

Answer: Yes. Since a subroutine is not required to preserve temporary registers
the main program must store register $t3 on the stack if it needs to preserve
it value across the call to subroutine A.

b) If subroutine A needs to use register $t4, does it need to save it on the
stack first? Explain.

Answer: No. Since subroutine A is not required to preserve temporary registers,
it can use register $t4 without having to save it on the stack first.

c) Once it starts executing, does subroutine A need to save $sp, $fp, and $ra on
the stack? Explain.

Answer: Yes. Since subroutine A calls subroutine B it needs to preserve
registers $sp, $fp, and $ra.

d) If the main program needs to pass two additional arguments to subroutine A
beyond those passed in registers $a0 to $a3, and if those arguments are stored
in registers $t5 and $t6, show the sequence of instructions that must be
executed immediately before the subroutine call. Include the subroutine call in
the sequence of instructions.

Answer:

addi        $sp,$sp,-8
sw        $t5,4($sp)
sw        $t6,0($sp)
jal        subroutine_A

e) While executing subroutine A, the subroutine needs to access the argument
that was originally stored in register $t6. Assuming subroutine A saves
registers $s0 to $s2 on the stack, show the assembly instruction that can be
used to retrieve this argument. Explain using a stack diagram.

Answer: The following diagram shows the stack during the execution of subroutine
A:

$t5
$t6
----
$s0        <-- $fp
$s1
$s2        <-- $sp

The argument that was originally stored in register $t6 can be accessed by
executing the following instruction:         lw        $t6,4($fp) or lw        $t6,12($sp)

------------------------------

V3) The main portion of a MIPS assembly program contains a call to a subroutine
A. Subroutine A does not call any other subroutine and returns to the main
program once it completes execution.

a) If the main program has important data stored in register $t5, does it need
to save it on the stack before calling subroutine A? Explain.

Answer: Yes. Since a subroutine is not required to preserve temporary registers
the main program must store register $t5 on the stack if it needs to preserve
it value across the call to subroutine A.

b) If subroutine A needs to use register $s6, does it need to save it on the
stack first? Explain.

Answer: Yes. Since a subroutine must preserve all saved registers that it will
use, it must save $s6 on the stack before using it.

c) Once it starts executing, does subroutine A need to save $sp, $fp, and $ra on
the stack? Explain.

Answer: No. Since subroutine A does not call another subroutine, it does not
need to save $sp, $fp, or $ra.

d) If the main program needs to pass four additional arguments to subroutine A
beyond those passed in registers $a0 to $a3, and if those arguments are stored
in registers $t0, $t1, $t2, and $t3, show the sequence of instructions that
must be executed immediately before the subroutine call. Include the subroutine
call in the sequence of instructions.

Answer:

addi        $sp,$sp,-16
sw        $t0,12($sp)
sw        $t1,8($sp)
sw        $t2,4($sp)
sw        $t3,0($sp)
jal        subroutine_A

e) While executing subroutine A, the subroutine needs to access the argument
that was originally stored in register $t0. Assuming subroutine A saves
registers $s4 to $s7 on the stack, show the assembly instruction that can be
used to retrieve this argument. Explain using a stack diagram.

Answer: The following diagram shows the stack during the execution of subroutine
A:

$t0
$t1
$t2
$t3
----
$s4        <-- $fp
$s5
$s6
$s7        <-- $sp

The argument that was originally stored in register $t0 can be accessed by
executing the following instruction:         lw        $t0,16($fp) or         lw        $t0,28($sp)

--------------------------------

V4) The main portion of a MIPS assembly program contains a call to a subroutine
A. At some point, subroutine A calls subroutine B and returns to the main
program once both subroutines have completed execution.

a) If the main program has important data stored in register $s0, does it need
to save it on the stack before calling subroutine A? Explain.

Answer: No. The main program does not need to store register $s0 since it will
be preserved (i.e. saved and later restored) by subroutine A.

b) If subroutine A needs to use register $s4, does it need to save it on the
stack first? Explain.

Answer: Yes. Since a subroutine must preserve all saved registers that it will
use, it must save $s4 on the stack before using it.

c) Once it starts executing, does subroutine A need to save $sp, $fp, and $ra on
the stack? Explain.

Answer: Yes. Since subroutine A calls subroutine B it needs to preserve
registers $sp, $fp, and $ra.

d) If the main program needs to pass five additional arguments to subroutine A
beyond those passed in registers $a0 to $a3, and if those arguments are stored
in registers $t0 to $t4 show the sequence of instructions that must be executed
immediately before the subroutine call. Include the subroutine call in the
sequence of instructions.

Answer:

addi        $sp,$sp,-20
sw        $t0,16($sp)
sw        $t1,12($sp)
sw        $t2,8($sp)
sw        $t3,4($sp)
sw        $t4,0($sp)
jal        subroutine_A

e) While executing subroutine A, the subroutine needs to access the argument
that was originally stored in register $t1. Assuming subroutine A saves
registers $s5 to $s7 on the stack, show the assembly instruction that can be
used to retrieve this argument. Explain using a stack diagram.

Answer: The following diagram shows the stack during the execution of subroutine
A:

$t0
$t1
$t2
$t3
$t4
----
$s5        <-- $fp
$s6
$s7        <-- $sp

The argument that was originally stored in register $t0 can be accessed by
executing the following instruction:         lw        $t1,16($fp) or         lw        $t1,24($sp)

=========================================================================================================

Question 3: PIC Assembly

V1) Consider the following sequence of PIC16F84 assembly instructions. If the
carry flag is initially clear, what is the final value stored in register 15?

                MOVLW                153
                MOVWF                15
                MOVLW                5
                MOVWF                16
LABEL:        RRF                15,1
                DECFSZ        16,1
                GOTO                LABEL
                SWAPF                15,1

Answer: This sequence of instructions initializes register 15 to 153 (99H),
rotates the bits of the register 5 bit positions to the right, and swaps the
upper and lower four bits. The final value stored in register 15 is: 49H = 73


V2) Consider the following sequence of PIC16F84 assembly instructions. If the
carry flag is initially set, what is the final value stored in register 15?

                MOVLW                177
                MOVWF                15
                MOVLW                5
                MOVWF                16
LABEL:        RLF                15,1
                DECFSZ        16,1
                GOTO                LABEL
                SWAPF                15,1

Answer: This sequence of instructions initializes register 15 to 177 (B1H),
rotates the bits of the register 5 bit positions to the left, and swaps the
upper and lower four bits. The final value stored in register 15 is: B3H = 179

V3) Consider the following sequence of PIC16F84 assembly instructions. If the
carry flag is initially clear, what is the final value stored in register 15?

                MOVLW                203
                MOVWF                15
                MOVLW                5
                MOVWF                16
LABEL:        RRF                15,1
                DECFSZ        16,1
                GOTO                LABEL
                COMF                15,1

Answer: This sequence of instructions initializes register 15 to 203 (CB H),
rotates the bits of the register 5 bit positions to the right, and complements
the bits. The final value stored in register 15 is: 49H = 73

V4) Consider the following sequence of PIC16F84 assembly instructions. if the
carry flag is initially set, what is the final value stored in register 15?

                MOVLW                98
                MOVWF                15
                MOVLW                5
                MOVWF                16
LABEL:        RLF                15,1
                DECFSZ        16,1
                GOTO                LABEL
                COMF                15,1

Answer: This sequence of instructions initializes register 15 to 98 (62H),
rotates the bits of the register 5 bit positions to the left, and complements
the bits. The final value stored in register 15 is: A9H = 169