EECE 370

THREE-PHASE CIRCUITS

Three-phase electric power is a common method of electric power transmission. It is a type of polyphase system mainly used to power motors and many other devices. A three-phase system uses less conductor material to transmit electric power than equivalent single-phase, two-phase, or direct-current systems at the same voltage.

In a three-phase system, three circuit conductors carry three alternating currents (of the same frequency) which reach their instantaneous peak values at different times. Taking one conductor as the reference, the other two currents are delayed in time by one-third and two-thirds of one cycle of the electrical current. This delay between "phases" has the effect of giving constant power transfer over each cycle of the current, and also makes it possible to produce a rotating magnetic field in an electric motor.

Single-phase loads:

Single-phase loads may be connected to a three-phase system, either by connecting across two live conductors (a phase-to-phase connection), or by connecting between a phase conductor and the system neutral, which is either connected to the center of the Y (star) secondary winding of the supply transformer, or is connected to the center of one winding of a delta transformer (Highleg Delta system) (see transformer and Split phase ). Single-phase loads should be distributed evenly between the phases of the three-phase system for efficient use of the supply transformer and supply conductors.

The line-to-line voltage of a three-phase system is √3 times the line to neutral voltage. Where the line-to-neutral voltage is a standard utilization voltage, (for example in a 240 V/415 V system) individual single-phase utility customers or loads may each be connected to a different phase of the supply. Where the line-to-neutral voltage is not a common utilization voltage, for example in a 347/600 V system, single-phase loads must be supplied by individual step-down transformers. In multiple-unit residential buildings in North America, lighting and convenience outlets can be connected line-to-neutral to give the 120 V distribution voltage (115V utilization voltage), and high-power loads such as cooking equipment, space heating, water heaters, or air conditioning can be connected across two phases to give 208 V. This practice is common enough that 208 V single-phase equipment is readily available in North America. Attempts to use the more common 120/240 V equipment intended for three-wire single-phase distribution may result in poor performance since 240 V heating equipment will only produce 75% of its rating when operated at 208 V.

Three-phase loads:

The most important class of three-phase load is the electric motor. A three phase induction motor has a simple design, inherently high starting torque, and high efficiency. Such motors are applied in industry for pumps, fans, blowers, compressors, conveyor drives, and many other kinds of motor-driven equipment. A three-phase motor will be more compact and less costly than a single-phase motor of the same voltage class and rating; and single-phase AC motors above 10 HP (7.5 kW) are uncommon. Three phase motors will also vibrate less and hence last longer than single phase motor of the same power used under the same conditions.

An interesting example of a three-phase load is the electric arc furnace used in steelmaking and in refining of ores.

Advantages of three-phase loads:

Often the advantages of 3 phase motors, and other 3 phase equipment, make it smart and easily worthwhile to convert single-phase power to generate 3 phase with a Rotary Phase Converter. Small and large customers, such as residential, rural businesses, or farm properties may not have access to a 3 phase supply, or may not want to pay for the extra cost of a 3 phase service, but may still wish to use 3 phase equipment. Such 3 phase converters may also allow the frequency (see also frequency converters) to be varied allowing for different equipment frequency requirements (50Hz, 60Hz, 400Hz, etc.) and also for motor speed control (VFDs).  Some locomotives are driven by 3-phase motors with 3 phase converters converted from the incoming supply of either DC or 1 phase AC.   The two main types of 1 phase to 3 phase converters are Rotary Phase Converters and Static Phase Converters.  Click here to read more about 3 phase converters.