AMERICAN UINVERSITY OF BEIRUT

FACULTY OF ENGINEERING AND ARCHITECTURE

EECE 460 Control Systems

Fall 2006-2007

Quiz I

Prof. Fouad Mrad

1.5 Hours, Nov 2, 2006

Total 100 points;

Open Book Exam, 2 pages

Problem 1 (20 points):

Consider the system shown in the Figure below.

Control system with unity feedback

- Supply the open loop transfer function, discuss stability.

- Supply the closed loop transfer function, discuss stability.

- List effect of the unity feedback on the O.L.T.F.? Explain.

- Assume that there is a Proportional controller of gain K that can vary positively from 0 to infinity in series with G(s), based on the root locus of the system:

  - Which part of the real axis of the s-plane is possible location of the closed loop transfer function poles?

  - For every value of the P controller gain, how many poles are there for the C.L.T.F.?

  - As K is infinitely increased, suggest the convergence values of the C.L.T.F. poles

Problem 2 (30 points):

Consider the system shown in the Figure below.

Control System with series controller

- If the Controller transfer function was unity, supply when valid the:

- O.L.T.F. step response Maximum Overshoot and settle time

- C.L.T.F. step response Maximum Overshoot and settle time

- If the Controller transfer function was a PD = (S+5), supply when valid the:

- O.L.T.F. step response Maximum Overshoot and settle time

- C.L.T.F. step response Maximum Overshoot and settle time

- Design a P controller if possible for the controlled system:

- Overdamped

- Critically damped

- Underdamped

- Undamped

Problem 3(50 points):

Consider the design of a regulator for the following model:

where

- Get the equivalent transfer function modeling the same process

- What are the poles of the system? Is it stable? Why.

- What are the eigenvalues of the matrix A?

- What are the system step response overshoot and settle time?

- Suppose that we designed the input U(t) as a function of the states feedback with gain vector K (i.e. U(t) = -Kx(t)),design if possible a K vector [k1  k2] such that the newly (controlled system) equivalent matrix (A-BK) has desired eigenvalues -1.8 +j2.4 and -1.8 -j2.4.

- What are the achieved poles and step response overshoot and settle time (if defined) of the controlled system (part 5)?