AMERICAN UINVERSITY OF BEIRUT

FACULTY OF ENGINEERING AND ARCHITECTURE

EECE 460 Control Systems

Fall 2006-2007. Quiz I SOLUTION

Prof. Fouad Mrad

Problem 1 (20 points):

a)   O.L.T.F =

Poles at: 0, -5, -1±3i

All poles are in LHP but one pole is at the origin => marginally stable

b)   C.L.T.F  =

Poles at: -5.032, -0.0198, -0.9743± 3.018i

All poles in LHP => stable

c) Advantages:

- In this problem’s case: move the system from being marginally stable to stable

-tune input to get desired output

-system response becomes insensitive to external disturbances and internal

variations of system parameters

d) zeros: -1; poles: 0, -1±3i, -5

d.1) two intervals (-∞,-5) and (-1,0)

d.2) 4

d.3) -1 and ∞

Problem 2 (30 points):

a.1)     O.L.T.F =

; =>  > 1 => over damped

Using the 2% criterion:

Mp does not exist

a.2)	C.L.T.F =

=>  > 1 => over damped

Using the 2% criterion:

Mp does not exist

b.1) 	O.L.T.F =

T = 1 => ts = 4T = 4sec; Mp does not exist

b.2) 	C.L.T.F =

T=1/2; ts = 2

Mp does not exist

c)        O.L.T.F =  => C.L.T.F

; =>

c.1) over damped =>   > 1 => k < 4 (no unique value)

c.2) critically damped =>   = 1 => k = 4

c.3) under damped =>   < 1 => k > 4 (no unique value)

c.4) undamped =>   = 0 => not possible

Problem 3 (50 points):

1) tf = C(SI-A)-1B =

2) roots = ± 4.5387 => not stable

3) det|λI-A|=0 => det=> λ = ± 4.54

4) System not stable => step response overshoot and settle time do not exist

5) det|λI-(A-BK)|=0

A-BK =  =

Thus =0

=> 2-k2 + k1 – 20.6 = 0

Case 1: for  = -1.8 + 2.4j, k1 =29.6 & k2 =3.6

Case 2: for  = -1.8 - 2.4j, k1 =29.6 & k2 =3.6 (same result)

6)The achieved poles are the eigen values of the function, e.g. -1.8±2.4j

denomenator = (s-1)( s-2) = s2 + 3.6s + 9; =>  (under damped)

ts =