Faculty of Engineering and Architecture

American University of Beirut

CIVE 420 – Concrete I

Assignment # 2

Problem: I

(	Equilibrium of forces:

(	Check if Tension steel yielded:

= 0.011 > (y = 0.002 ( Tension steel yielded

(	Check if compression steel yielded:

( comp. Steel didn’t yield as assumed.

(

(	Equilibrium of forces:

( 7080.5 c2 – 75408 c – 110640 = 0

( c = 11.95 cm	and  a = (1c  =  10.16 cm

(	Calculate ultimate flexural resistance Mu:

where

( Mn = 51.65 T – m

hence Mu =  (Mn = 0.9Mn = 46.49 T-m

(	Check Maximum Reinforcement Ratio:

Since ( ( (max  (  our section satisfies ductility requirements of ACI.

Problem: II

i)

assume a < 25cm

(	Equilibrium of forces:

T = Cc

Asfy = 0.85 f’c (60) a + 0.85 f’c (a – 10) (30)

(	Check if tension steel  yielded as assumed:

( Tension steel yielded as assumed

(	Find ultimate flexural capacity:

= 172.39 T-m

Mu = ( Mn = 0.9 Mn = 155.15 T-m

(	Check Ductility Requirements:

cb = 0.6 d  (for grade 60 steel)

cmax = 0.75 cb = 0.75  0.6  80 = 36 cm

Since  c = 22 cm < cmax  (  section satisfies ductility requirements.

ii)

A’s = 58.9

(	Equilibrium of forces:

T = Cc

Asfy = 0.85 f’c (60) (2) + 0.85f’c (30) (2 – 10) + A’sfy

(	Check if compression steel bars yielded as assumed

3 < 5.413 ( comp. Steel bars yielded as assumed

No need to check for tension steel bars since they yielded with c = 22 cm

( for  c = 16.24 cm,  they will definitely be in the yielding range

(	Find ultimate flexural capacity:

(  Mn = 182.90 T-m

Mu = (Mn = 0.9 Mn = 164.6 T-m

(	Check Ductility Requirements:

cmax = 0.75 cb = 36 cm

c = 16.24cm < 36cm ( Ductility Requirements are satisfied

Actually compression reinforcements improve ductility

Problem: III

| Assume c = 15 cm (1 = 0.85 for f’c = 210 Kg/cm2 a = 12.75 cm |  | ( ( ( ( ( ( ( ( ( ( ( ( | (1) (2) (3) (4) (5) |
| --- | --- | --- | --- |

(	Calculate stresses and strains in the steel layers:

(  fs1 = fy = 4200 kg/cm2

fs2 = Es2  (s2 = 2  106  0.001 = 2000 kg/cm2

(s3 = (cu (d - c) = 0.004 > 0.002

Since layer 3 yields ( the remaining layers will yield

( fs3 =  fs4 = fs5 = fy = 4200 kg/cm2

T    = (As3 + As4 + As5) fy + As2 fs2

= (7 T20) (4200)  +  (2T20) (2000)

= 104.9 T

Cc = 0.85 f’c (30) (12.75) + As1fy

= 107.8 T

(	Calculate Nominal Flexural capacity:

Mn =  As5  fy (65) + As4 fy (50) + As3 fy (35)

+ As2 fs2(20) – 0.85 f’c (30) (12.75)– As1 fy (5) = 44.3 T-m

Problem: IV

WL = 0.75 T/m   ,   Ws = 1.0 T/m

Wg  = 0.3  0.4  2.5 = 0.3 T/m

WD = Wg + Ws = 1.3 T/m

( Wu = 1.4 WD + 1.7 WL = 3.095 T/m   ~ 3.1 T/m

( Wn == 3.44 T/m

3.1 T/m

(	Designing for Top Reinforcement: ( -ve moment)

Assume d = 35 cm

Mu = -6.2 T-m

=  0.00472		since (min < ( <(max  ( o.k

=  4.956 cm2    5cm2

( use (5 T 12)  (  (5.65 cm2)

(	Designing for bottom reinforcement: ( +ve Moment)

Also  assume d = 85 cm

Mu = 3.48 T-m

( use  (min = 0.00333

( As(bottom) = (0.00333) (30) (35) = 3.496 cm2       3.5 cm2

( use 5T10  (  (3.926 cm2)

(	Find (max and (min

# Text boxes

Shear

Diagram

3.48 T-m

-6.2  T-m

-6.2  T-m

Moment

Diagram

-7.75 T

-6.2 T

6.2 T

7.75 T TT