Chapter 10

Memory Management

- The memory management portion of the Operating System is responsible for the efficient usage of main memory, especially in a multiprogramming environment where processes contend for memory.

- It must also offer protection of one process address space from another (including protection of system address space from user processes).

- The memory subsystem should also provide programmers with a convenient logical or virtual address space, in which the low-level details of memory management are hidden.

Sharing of Memory

Issues

- Allocation schemes

- Protection from each other

- Protecting OS code

- Translating logical addresses to physical

- Swapping programs

- What if physical memory is small: Virtual memory

Memory Management Strategies

- Fetch Strategy: 
Determine when to load and how much to load at a time. E.g., demand fetching, anticipated fetching (pre-fetching).

- Placement (or allocation) Strategy:
Determine where information is to be placed.
E.g., Best-Fit, First-Fit, Buddy-System.

- Replacement Strategy: 
Determine which memory area is to be removed under contention conditions.
E.g., LRU, FIFO.

Memory Management Evolution

- Variations

  - Fixed Partitions

  - Variable Partitions

  - Segmentation

  - Paging

- Criteria

  - How efficiently can it be implemented?

  - How effectively can the physical memory be utilized?

Fixed Partitions

- Divide all physical memory into a fixed set of contiguous partitions. E.g., early IBM 360 models.

+---------+
  	 |  12K    |  Queue for waiting processes
  	 +---------+
  	 |  2K     |    ....
  	 +---------+
  	 |  6K     |    ....
  	 +---------+
  	 | OS: 2K  |

+---------+

- Place only one process at a time in any partition.

- Bind physical to virtual address during loading, not during execution.

- Partition boundaries limit the available memory for each process.

- A process is either entirely in main memory or entirely on backing store (i.e., swapped in or swapped out).

- A process may only be swapped into the same partition from which it was swapped out (why?)

- It can only simulate smaller, not larger, virtual space than physical space.

- No sharing between processes.

- Should there be a single queue per partition or one global queue?

10 Memory space wasted:

  - Internal fragmentation: memory which is internal to a partition, but not used.

  - External fragmentation: a partition is unused and available, but too small for any waiting job.

Managing Free Space: Linked Lists

- Each record has

  - Process ID/ Free (H: hole)

  - Start location

  - Size

  - Pointer to Next record

- Current state (H,2,3),(B,5,5),(H,10,2),(D,12,2),(H,14,6)

- How should we update the list when B leaves?

Managing Free Space: Linked Lists

- Current state (H,2,3),(B,5,5),(H,10,2),(D,12,2),(H,14,6)

- PCB for a process can have a pointer into the corresponding record

- When a process terminates, neighboring blocks need to be examined

  - Doubly-linked lists

Allocation Strategy

- Suppose a new process requests 15K, which hole should it use?

- First-fit: 30K hole

- Best-fit: 20K hole

- Worst-fit: 60K hole

- Let {Hi | i = 1,…,n} be unused blocks and k be the size of a requested block.

- First-Fit

- Select the first Hi such that size (Hi) ³ k.

- That is, select the first block that is big enough

- Best-Fit

- Select Hi such that size (Hi) ³ k and, if size (Hj) ³ k then size (Hj) ³ size (Hi) for i ¹ j.

- That is, select the smallest block that is big enough.

- Worst-Fit

- Select Hi such that size (Hi) ³ k, and if size(Hj) ³ k then size(Hj) ³ size(Hi) for i ¹ j.   (idea: to produce the largest left-over block.)

- Buddy System

Best-fit vs. First-fit

- Both could leave many small and useless holes.

- To shorten search time for First-Fit, start the next search at the next hole following the previously selected hole.

- Best-Fit performs better:  Assume holes of 20K and 15K, requests for 12K followed by 16K can be satisfied only by best-fit

- First-Fit performs better: Assume holes of 20K and 15K, requests for 12K, followed by 14K, and 7K, can be satisfied only by first-fit

- In practice, F-F is usually  better than B-F, and F-F and B-F are better than W-F.

-Allocation algorithm that forms basis of Linux memory management

- Suppose we have 128 units (128 pages or 128K)

- Each request is rounded up to powers of 2

- Initially a single hole of size 128

- Suppose, A needs 6 units, request rounded up to 8

- Smallest hole available: 128. Successively halved till hole of size 8 is created

- At this point, holes of sizes 8, 16, 32, 64

- Next request by B for 5 units: hole of size 8 allocated

-Next request by C for 24 units: hole of size 32 allocated

Chapter 11

Lecture Note: Virtual Memory

- Recall: memory allocation with variable partitions requires mapping logical addresses to physical addresses

- Virtual memory achieves a complete separation of logical and physical address-spaces

Today, typically a virtual address is 32 bits, this allows a process to have 4GB of virtual memory

  - Physical memory is much smaller than this, and varies from machine to machine

  - Virtual address spaces of different processes are distinct

- Structuring of virtual memory

  - Paging: Divide the address space into fixed-size pages

  - Segmentation: Divide the address space into variable-size segments (corresponding to logical units)

Paging (1)

The position and function of the MMU

Virtual Memory (Paging)

- Physical memory is divided into chunks called page-frames (on Pentium, each page-frame is 4KB)

- Virtual memory is divided into chunks called pages; size of a page is equal to size of a page frame

  - So typically, 220 pages (a little over a million) in virtual memory

- OS keeps track of mapping of pages to page-frames

- Some calculations:

  - 10-bit address : 1KB of memory; 1024 addresses

  - 20-bit address : 1MB of memory; about a million addresses

  - 30-bit address : 1 GB of memory; about a billion addresses

Virtual Memory in Unix

Paging

- A virtual address is considered as a pair (p,o)

- Low-order bits give an offset o within the page

- High-order bits specify the page p

- E.g. If each page is 1KB and virtual address is 16 bits, then low-order 10 bits give the offset and high-order 6 bits give the page number

- The job of the Memory Management Unit (MMU) is to translate the page number p to a frame number f

- The physical address is then (f,o), and this is what goes on the memory bus

- For every process, there is a page-table (basically, an array), and page-number p is used as an index into this array for the translation

Page Table Entry

- Validity bit: Set to 0 if the corresponding page is not in memory

- Frame number

- Number of bits required depends on size of physical memory

- Protection bits:

- Read, write, execute accesses

- Referenced bit is set to 1 by hardware when the page is accessed: used by page replacement policy

- Modified bit (dirty bit) set to 1 by hardware on write-access: used to avoid writing when swapped out

Page  Tables (1)

Internal operation of MMU with 16 4 KB pages

Design Issues

- What is the “optimal” size of a page frame ?

- Typically 1KB – 4KB, but more on this later

- How to save space required to store the page table

- With 20-bit page address, there are over a million pages, so the page-table is an array with over million entries

- Solns: Two-level page tables, TLBs (Translation Lookaside Beffers), Inverted page tables

- What if the desired page is not currently in memory?

- This is called  a page fault, and it traps to kernel

- Page daemon runs periodically to ensure that there is enough free memory so that a page can be loaded from disk upon a page fault

- Page replacement policy: how to free memory?

Multi-Level Paging

- Keeping a page-table with 220 entries in memory is not viable

- Solution: Make the page table hierarchical

- Pentium supports two-level paging

- Suppose first 10-bits index into a top-level page-entry table T1 (1024 or 1K entries)

- Each entry in T1 points to another, second-level,  page table with 1K entries (4 MB of memory since each page is 4KB)

- Next 10-bits of physical address index into the second-level page-table selected by the first 10-bits

- Total of 1K potential second-level tables, but many are likely to be unused

- If a process uses 16 MB virtual memory then it will have only 4 entries in top-level table (rest will be marked unused) and only 4 second-level tables

Paging in Linux

Linux uses three-level page tables

Translation Lookaside Buffer (TLB)

- Page-tables are in main memory

- Access to main memory is slow compared to clock cycle on CPU (10ns vs 1 ns)

- An instruction such as MOVE REG, ADDR has to decode ADDR and thus go through page tables

- This is way too slow !!

- Standard practice: Use TLB stored on CPU to map pages to page-frames

- TLB stores small number (say, 64) of page-table entries to avoid the usual page-table lookup

- TLB is associative memory and contains, basically, pairs of the form (page-no, page-frame)

- Special hardware compares incoming page-no in parallel with all entries in TLB to retrieve page-frame

- If no match found in TLB, standard look-up invoked

More on TLB

- Key design issue: how to improve hit rate for TLB?

- Which pages should be in TLB: most recently accessed

- Who should update TLB?

- Modern architectures provide sophisticated hardware support to do this

- Alternative:  TLB miss generates a fault and invokes OS, which then decides how to use the TLB entries effectively.

Inverted Page Tables

- When virtual memory is much larger than physical memory, overhead of storing page-table is high

- For example, in 64-bit machine with 4KB per page and 256 MB memory, there are 64K page-frames but 252 pages !

- Solution: Inverted page tables that store entries of the form (page-frame, process-id, page-no)

- At most 64K entries required!

- Given a page p of process x, how to find the corresponding page frame?

- Linear search is too slow, so use hashing

- Note: issues like hash-collisions must be handled

- Used in some IBM and HP workstations; will be used more with 64-bit machines

Hashed  Page Tables

Steps in Paging

- Today’s typical systems use TLBs and multi-level paging

- Paging requires special hardware support

- Overview of steps

- Input to MMU: virtual address  = (page p, offset o)

- Check if there is a frame f with (p,f) in TLB

- If so, physical address is (f,o)

- If not, lookup page-table in main memory ( a couple of accesses due to multi-level paging)

- If page is present, compute physical address

- If not, trap to kernel to process page-fault

- Update TLB/page-table entries (e.g. Modified bit)

# Text boxes

A exits

The relation between virtual

Addresses and physical memory

addresses given by page table.

4H

4D

8B

8H

32C

8H

B exits

64H

4H

4D

16H

8H

64H

32C

D requests 3

4D

Protection bits

Modified bit

Frame number

Page number

4H

8H

8B

PID

PID

Hash table

Number of entries: Number of page frames

Frame #

Page #

Hash

Offset

Page number

8A

32C

64H

8B

8A

16H

32C

64H