H.U. Fall 2008								  	Dr. H. Barsoumian

## PHY 218

## Quiz I

1.	For the circuit shown in the figure

- Write down the KCL equations.			( 4  pts)

- Write down the KVL equations.			( 9 pts)

- Argue (without algebra) that	  I4 = 0			( 4 pts)

- Show that I1 =  40mA for  R=100 &  V =12v 	(3 pts)

--------------------------------------------------------------------------------------

2.	Take R = 1.5K and Vi = 15v

a.	Calculate the current   I1.   				( 12  pts)

b.	Is impedance matching satisfied? Explain briefly.	(3 pts)

---------------------------------------------------------------------------------------

3.	Use the Thevenin’s Theorem to show that circuit (b) is equivalent       to circuit (a).  Note: NO points for other methods.            (15 points)

-------------------------------------------------------------------------

4.	Which of the four spectra belongs to the waveform?

Explain your answer clearly.

(No explanation, no points)		 ( 8  points)

----------------------------------------------------------------------------------------------------------------------------------------------

5.	Answer 7 of the following 11 questions. The 8th answer will be ignored.	 ( 7x6 = 42  points)

- Why do transmission lines have capacitance and inductance?

- What is the value of a resistor marked as 3K3?

- Why does the size of capacitors increase with their value, whereas that of resistors does not?

- Why the value of an electrolytic capacitor is depends a little on voltage?

- Argue that Ce ~ 1.4C is an “educated guess” for the connection shown, irrespective of X.

- How is a data “written” on a CD?

- Mention three uses of transformers.

- What is the shape of the Bode diagram for the filter shown?

- Define “termination” in transmission lines

- What is the approximate value of a current that causes painful shock?

- Complete the following: Quality factor  Q = (energy -------)/(energy -------)

-----------------------------------------------------------------------------------------------------------------------------------------

### Good Luck!								     20 + 2x15 + 8 + 42 = 100