String Primitive instructions:

Five groups of instructions are used to copy from memory location pointed to by ESI to memory location pointed to by EDI. Although they are called string primitive, they are not only limited to character arrays. These instructions are described in the follows:

MOVSB , MOVSW, MOVSD: copy data from memory location pointed to by ESI to memory location pointed to by EDI. The two registers are incremented or decremented automatically based on a special flag called the Direction Flag.

Value of Direction flag	Effect on ESI & EDI

Clear	increment

Set	decrement

CLD is an instruction used to clear the direction flag.

STD is an instruction used to set the direction flag.

Instruction	Value of ESI & EDI incremented

MOVSB (BYTE )	1

MOVSW (WORD)	2

MOVSD (DOUBL WORD)	4

The String primitive instructions perform a single memory copy. If multiple copy is needed, the REPeat instruction is used. REP instruction repeats an instruction as long as ECX > 0.

Instruction 	Description

REP	Repeat while ECX > 0

REPZ, REPE	Repeat while the Zero Flag is set and ECX > 0.

REPNZ, REPNE	Repeat while the Zero flag is clear and ECX > 0.

Example:

.data

Source DWORD 20 DUP (0FFFFFFFFh)

Target  DWORD 20 DUP (?)

.code

Cld

Mov ecx, LENGHTOF source

Mov esi, OFFSET source

Mov edi, OFFSET target

Rep movsd	; copy double words while ecx > 0.

CMPSB, CMPSW, and CMPSD: compare a memory location pointed to by ESI to a memory location pointed to by EDI.

Example:

.data

Source DWORD 1234h

Target  DWORD 5678h

.code

Mov esi, OFFSET source

Mov edi, OFFSET target

Cmpsd

Ja L1

Jmp L2

To compare multiple locations, then set ecx to the length of the array (as a counter) and use the Repeat instruction.

Example:

.data

Source DWORD 1234h

Target  DWORD 5678h

.code

Mov esi, OFFSET source

Mov edi, OFFSET target

CLD	; direction is up (increment)

Mov ecx, LENGTHOF source

REPE Cmpsd

It repeats comparison until either ecx is zero or any pair of doublewords are different.

Example:

TITLE Comparing Strings             (Cmpsb.asm)

; This program uses CMPSB to compare two strings

; of equal length.

INCLUDE Irvine32.inc

.data

source BYTE "MARTIN  "

dest   BYTE "MARTINEZ"

str1   BYTE "Source is smaller",0dh,0ah,0

.code

main PROC

cld	; direction = up

mov  esi,OFFSET source

mov  edi,OFFSET dest

mov  cx,LENGTHOF source

repe cmpsb

jb   source_smaller

jmp  quit

source_smaller:

mov  edx,OFFSET str1

call WriteString

quit:

exit

main ENDP

END main

SCASB, SCASW, and SCASD:

The instructions SCASB, SCASW, and SCASD instructions compare a value in AL/AX/EAX to a byte, word, or doubleword, respectively, addressed by EDI.

These instructions are useful when looking for a single value in a long string.

When used with REPE, the string or array is scanned while ECX > 0 and the value in AL/AX/EAX matches each subsequent value in memory.

When used with REPNE, the string or array is scanned until either AL/AX/EAX matches a value in memory or ECX = 0.

Example:

Search a string alpha, looking for the letter F. If the letter is found, EDI points one position beyond the matching character. If the letter is not found, the JNZ instruction would exit:

Include Irvine32.inc

.data

Alpha BYTE "ABCDEFGH",0

Msg BYTE "NOT FOUND",0

Msg1 BYTE "FOUND",0

.code

main PROC

Mov edi, OFFSET alpha

Mov al, 'F'

Mov ecx, LENGTHOF alpha

Cld

Repne scasb

Jnz quit1

Dec edi

mov edx, offset msg1

call writestring

jmp quit

quit1:   mov edx, offset msg

call writestring

quit:	exit

main ENDP

END main

STOSB, STOSW, STOSD:

Store the contents of AL/AX/EAX, respectively, in memory locations pointed to be EDI. EDI is incremented /  decremented based on the Direction flag. When used with REP prefix, these instructions fills all elements of the string or array with a single value. For example, the following code initializes each byte in string1 to 0FFh:

.data

Count = 100

String1 Byte Count Dup (?)

.code

Mov al, 0FFh

Mov edi, offset string1

Mov ecx, Count

Cld

Rep stosb

LODSB, LODSW, and LODSD:

These instructions load a byte, a word or a double word from memory at ESI into AL/AX/EAX, respectively. Also ESI is incremented /  decremented based on the Direction flag. The REP prefix is rarely used with LODS… instructions.

The LODSB substitutes for the following two instructions (assuming that the Direction flag is clear):

Mov al, [esi]

Inc   esi

Example: The following program multiplies each element of a doubleword array by a constant value. LODSD and STOSD work together:

INCLUDE Irvine32.inc

.data

array DWORD 1,2,3,4,5,6,7,8,9,10	; test data

multiplier DWORD 10		; test data

.code

main PROC

cld 		; direction = up

mov esi,OFFSET array  		; source index

mov edi,esi		; destination index

mov ecx,LENGTHOF array		; loop counter

L1:	lodsd                   		; copy [ESI] into EAX

mul multiplier		; multiply by a value

stosd                   		; store EAX at [EDI]

loop L1

exit

main ENDP

END main