Exam.2 CIE200 – STATICS

Fall 2016 (10th November, 2015)

CLOSED BOOK, 1 HR 15 Minutes

Problem I:  (25 points)

For the structure shown in Figure I it is required to perform the following:

- Simplify the loadings and forces to a single resultant force and resultant couple at point A.

- Replace the resultant force and resultant couple of part (i) to a single resultant force along line AB.

Problem II: (25 points)

An L-shape Pipe is subjected to the distributed loads and forces as shown in Figure II. The Force F is in a plane parallel to the Z-Y plane.

- Determine the magnitude and directions of the resultant moment and resultant force at

point A due to the loadings shown in Figure II.

- Determine the magnitude of the component of the resultant moment of Part (i) about

axis AC. Express this component as Cartesian vector.

Problem III:  (25 points)

Determine the reaction components at Pins A and B of the Frame System shown in Figure III. The support at C is also a pin connection and D is a free end.

Problem IV:  (25 points)

The pipe system ABC shown in Figure IV is in equilibrium and is supported by a pin at A and by cable DC. Determine the reaction forces and moments at Pin A and the tension in cable DC necessary to maintain equilibrium of the pipe system.

# Text boxes

### Figure I

30

30

4.0m

2.0m

7.0m

3.5m

50

### Figure II

### Figure III

### Figure IV

4.5m

5.5m

4.0m

4.0m