| CIVE 210 | Statics | Exam 1 Part I v1 | Mon Nov 29, 10 | 1/2 |
| --- | --- | --- | --- | --- |

Problem #1: (50%)

The rigid homogeneous weightless bar ABCD is

supported by 3 cables AE, EB and FD as shown.

Cables are hinge supported at E and F.

A vertical 200N concentrated force is acting

at C as shown.

Answer the following questions:

- Draw a Free Body Diagram (10%).

- Determine cable FD force (10%).

- Determine cable AE force (10%).

- Determine cable EB force (10%).

- Determine the reactions at the hinge support E. Indicate magnitude and directions (10%).

- Draw a Free Body Diagram (10%).

- Determine cable FD force (10%).

∑M about E = 0, 200 * 8 – Tfd * 12 = 0

Tfd = 1600/12 = 133.33N

- Determine cable AE force (10%).

∑M about G = 0, 200 * 4 – Tae * 4/5 * 6 – Tae * 3/5 * 16 = 0

Tae = 500/9 = 55.55N

- Determine cable EB force (10%).

∑M about H = 0, 200 * 4 – Teb * 4/5 * 12 – Teb * 3/5 * 8 = 0

Tae = 500/9 = 55.55N

Determine the reactions at the hinge support E. Indicate magnitude and directions (10%).

∑Fx = 0, Ex = 0

∑Fy = 0, Ey = Tae*3/5 + Tbe*3/5 = 200/3 N = 66.66 N

# Text boxes

Tbe

Tae

C

200N

4

4

E

4

A

3/4 Hour Exam, Closed Books

F

B

D

4

3

H

G

C

3

Tae

Tbe

Tdf

4

4

4

A

4

E

D

B

200N

F

Ex

Ey

Tbe

Tae